## Slide 1: Lesson 3 Programming Sensors
© 2026 Incipe Academy Limited. All rights reserved.
PLK83 Regular Course
Programming with C++
Notes: Mostly coding today: input and if-else in a mini calculator and two classwork programs, then the same if-else logic applied to INCIPE Board sensors.

## Slide 2: Input, decisions, then real sensor data.
2
Lesson Overview
01
Quick review of Lesson 2
02
Example: mini calculator
03
Classwork: larger number & grades
04
Sensors: reading & cleaning data
05
Counting button presses
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 3: Input, process, output.
3
Quick Review
Input
The data that we enter or the computer gets from the environment via sensors.
Process
Our codes (orders) for the computer to process.
Output
The response from the computer after processing the codes.
FROM THE USER
while(Serial.available()==0){}
int a = Serial.parseInt();
Wait when there’s no input, then read it and store it in “a”.
FROM A SENSOR
incipe.main();
incipe.getTemperature();
Activate the sensors & sensor libraries, then read a value.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Also from Lesson 2: comments (// and /* */) are ignored by the compiler, and Serial.parseFloat() reads a decimal number.

## Slide 4: Compare, combine, decide.
4
Quick Review
COMPARE
Symbol | Meaning
== | Equals to
!= | Not equals to
<= | Smaller than or equal to
>= | Larger than or equal to
< | Smaller than
> | Larger than
Remember: = assigns a value; == compares two values.
COMBINE
&&
AND: both must be true
||
OR: any one is true
!
NOT
DECIDE
if (…) { } else if (…) { } else { }
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 5: Three questions before you code.
5
Example: Mini Calculator
1
How to ask users to input two numbers? How to store them?
Serial.println("Please type your first number.");
while(Serial.available()==0){}
int a = Serial.parseInt();
2
How to add the two numbers? Store it to where?
int sum = a+b;
3
How to show the answer?
Serial.print("The answer is:");
Serial.println(sum);
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Refer to note page 1. The second number is read the same way and stored in b.

## Slide 6: The full sketch.
6
Example: Mini Calculator
void setup() {
Serial.begin(9600);
}
void loop() {
Serial.println("Please type your first number.");
while(Serial.available()==0){}
int a = Serial.parseInt();
Serial.println(a);
Serial.println("Please type your second number.");
while(Serial.available()==0){}
int b = Serial.parseInt();
Serial.println(b);
int sum = a+b;
Serial.print("The answer is:");
Serial.println(sum);
}
INPUT
Two numbers from the serial monitor.
PROCESS
Add them and store the result in sum.
OUTPUT
Print the answer.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Try it: change + to -, * or / to make the calculator do other operations.

## Slide 7: Which number is larger?
7
Classwork 1
void loop() {
Serial.println("Please enter your first number.");
while(Serial.available()==0){}
int a = Serial.parseInt();
Serial.println(a);
Serial.println("Please enter your second number.");
while(Serial.available()==0){}
int b = Serial.parseInt();
Serial.println(b);
if(a>b){
Serial.print(a);
Serial.println(" is the larger number");
}
else{
Serial.print(b);
Serial.println(" is the larger number");
}
}
YOUR NOTES
Refer to your note page 2.
THINK ABOUT IT
What prints when both numbers are the same?
© 2026 Incipe Academy Limited. All rights reserved.
Notes: setup() is the same as the calculator: Serial.begin(9600). The original if branch printed Serial.println(a + " is the larger number") and then the sentence again; in Arduino, adding a number to text like that prints garbage, so it now matches the else branch. If a equals b, the else branch runs and says b is larger: a good prompt for an else if (a == b) extension.

## Slide 8: Turn a score into a grade.
8
Classwork 2
void loop() {
Serial.println("Please enter your score.");
while(Serial.available()==0){}
int score = Serial.parseInt();
Serial.println(score);
if(score>=85 && score<=100){
Serial.println("Your grade is A");
} else if(score>=75 && score<=84){
Serial.println("Your grade is B");
} else if(score>=60 && score<=74){
Serial.println("Your grade is C");
} else if(score<60){
Serial.println("Your grade is D");
} else {
Serial.println("The full mark should be 100, please enter again.");
}
}
GRADES
A
85 – 100
B
75 – 84
C
60 – 74
D
Below 60
Anything above 100 falls to else.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Refer to note page 2. setup() is Serial.begin(9600) as before. Extension: a negative score currently gets D; ask students how to send it to the else message too.

## Slide 9: One function per sensor.
9
Sensors
WHAT A SENSOR DOES
A sensor detects and measures changes in our environment and converts them into electrical signals, which can be used to provide information, control the outputs, or trigger some useful action.
Sensor | Function
Ultrasonic | incipe.getDistance() · cm
Temperature | incipe.getTemperature()
Humidity | incipe.getHumidity()
Light | incipe.getLightIntensity()
Air quality | incipe.getPPM()
Alcohol | incipe.getAlcoholPPM()
CO gas | incipe.getCOPPM()
Flame | incipe.getFlameIntensity()
Button | incipe.getButtonResponse() · 1 = pressed
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Examples only: the point is that each sensor gives the program a number to use in if-else. Flame: the value is resistance, so it goes down when there is fire. Air quality, alcohol and CO: students decide the grade boundaries themselves.

## Slide 10: Turn raw numbers into meaning.
10
Data Cleaning
Data cleaning is the process of fixing or removing incorrect or incomplete raw data. Here, we focus on how to interpret the raw data to make it more useful.
incipe.getLightIntensity()
700, 1000…
A raw reading means little on its own. if-else gives it a label people understand.
AIR QUALITY, IN PLAIN STEPS
if AQvalue < xxxx
print Good
else if AQvalue > xxxx and < xxxx
print Moderate
else
print Poor
Students choose the xxxx boundaries.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 11: At 30°C, what is shown at "temp1"?
11
Checkpoint 1
READ THE CODE
float temp = incipe.getTemperature();
if (temp>30){
incipe.onscreen("temp1", "hot");}
else if (temp<10){
incipe.onscreen("temp1", "cold");}
else {
incipe.onscreen("temp1", temp);}
ANSWER
30
WHY
30 is not larger than 30, and not smaller than 10. So else runs and shows the temperature itself.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Answer: 30 (the value of temp). The original slide wrote incipe.getTemperature without brackets; it is corrected to getTemperature() here. Point out that > does not include 30 itself.

## Slide 12: The light reading jumps from 100 to 1000. What shows at "light1"?
12
Checkpoint 2
READ THE CODE
float light = incipe.getLightIntensity();
if (light>=700){
incipe.onscreen("light1", "bright");}
else if (light>=300 && light<700){
incipe.onscreen("light1", "normal");}
else {
incipe.onscreen("light1", "dark");}
ANSWER
bright
WHY
1000 is larger than or equal to 700, so the first condition is true.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Answer: bright. Before the light was switched on, 100 would have shown dark. The original slide wrote Float (capital F) and getLightIntensity without brackets; both are corrected here.

## Slide 13: Count each press once.
13
Button
FIRST TRY
int a = 0;
if (incipe.getButtonResponse() == 1)
{
a=a+1;
Serial.println(a);
}
1 = true (pressed). loop() runs many times while you hold the button, so a keeps going up.
COUNT ON RELEASE
int a = 0;
bool detect = false; // set as false at beginning
if (incipe.getButtonResponse() == 1) // pressed
{
detect = true;
}
if (incipe.getButtonResponse() == 0 && detect == true)
{ // not pressed and detect is true
a=a+1;
Serial.println(a);
detect = false;
}
detect remembers the press; a goes up once, when you let go.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The explanations of why the first version over-counts and how detect fixes it are added for this slide. Teacher note: for the count to keep growing, int a and bool detect should be declared above setup() (global), not inside loop().

## Slide 14: Which sensor haven’t we introduced yet?
14
Checkpoint 3
COVERED SO FAR
Ultrasonic · Temperature & humidity · Light · Air quality · Alcohol · CO gas · Flame · Button
ANSWER
Sound sensor
WHY
It is the one sensor in the set not covered yet. It comes next.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 15: Four ideas we will learn next.
15
Sound Sensor · Preview
The sound sensor uses incipe.getSoundIntensity(). Its example sketch samples sound for a short time, stores the counts and averages them into Loud, Normal or Quiet.
Timer
PreviousTime = millis();
While loop
while (millis() - PreviousTime < SAMPLE_TIME) { … }
Array
float database[100];
For loop
for (int i = 1; i < 100; i++) { … }
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Full example sketch, for reference: const int SAMPLE_TIME = 10; unsigned long PreviousTime = 0; (the original wrote "unsigned double", which does not compile) int SoundDetect = 0; float database[100]; int count = 0; void setup() { Serial.begin(9600); } void loop() { PreviousTime = millis(); while (millis() - PreviousTime < SAMPLE_TIME) { if (incipe.getSoundIntensity() == 1) { SoundDetect++; } } database[count] = SoundDetect; SoundDetect = 0; count++; if (count == 100) { for (int i = 1; i < 100; i++) { database[0] = database[0] + database[i]; database[i] = 0; } float mean = database[0] / 100; Serial.println(mean); if (mean > 200) { Serial.println("Loud"); } else if (mean <= 200 && mean > 20) { Serial.println("Normal"); } else if (mean <= 20) { Serial.println("Quiet"); } database[0] = 0; count = 0; } }

## Slide 16: Three things to take away.
16
Recap
1
Wait, read, store: while(Serial.available()==0){} then Serial.parseInt().
2
if, else if & else with && turn a number into a decision, like a grade.
3
Sensor readings are just numbers: the same if-else turns them into labels.
Thank you!
© 2026 Incipe Academy Limited. All rights reserved.