## Slide 1: Lesson 4 Array & For Loop
© 2026 Incipe Academy Limited. All rights reserved.
PLK83 Regular Course
Programming with C++
Notes: Today: store many values in one array, then use a for loop to go through them. Sensors appear only as quick review examples.

## Slide 2: Store many values, then loop through them.
2
Lesson Overview
01
Quick review of Lesson 3
02
Array: create, write, read & clear
03
For loop
04
Array + for loop: average & largest value
05
Classwork: handling data
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 3: The mini calculator in three steps.
3
Quick Review
1
How to ask users to input two numbers? How to store them?
Serial.println("Please type your first number.");
while(Serial.available()==0){}
int a = Serial.parseInt();
2
How to add the two numbers? Store it to where?
int sum = a+b;
3
How to show the answer?
Serial.print("The answer is:");
Serial.println(sum);
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The second number is read the same way and stored in b. The full sketch runs inside loop(), with Serial.begin(9600) in setup().

## Slide 4: Sensor readings need cleaning.
4
Quick Review
FUNCTIONS FOR SENSORS
incipe.getTemperature()
incipe.getHumidity()
incipe.getDistance()
incipe.getLightIntensity()
incipe.getPPM()
incipe.getCOPPM()
incipe.getAlcoholPPM()
incipe.getFlameIntensity()
DATA CLEANING
Fixing or removing incorrect or incomplete raw data. Here, we focus on interpreting the raw data to make it more useful.
if AQvalue < xxxx
print Good
else if AQvalue > xxxx and < xxxx
print Moderate
else
print Poor
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Sensors are review examples only this lesson. The button counter and the sound sensor sketch from Lesson 3 are not repeated here; the sound sketch's array and for loop are what this lesson teaches.

## Slide 5: Which sensor does not require data cleaning?
5
Checkpoint 1
THINK ABOUT WHAT EACH GIVES BACK
incipe.getLightIntensity() → 700, 1000…
incipe.getPPM() → a ppm number
incipe.getButtonResponse() → 1 or 0
ANSWER
Button
WHY
It already gives 1 (pressed) or 0 (not pressed), so there is nothing to interpret.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The original poll did not list its options; Button is the clearest answer. Temperature and distance are also arguable, since they come back in °C and cm already.

## Slide 6: A collection of variables, like a database.
6
Array
22
24
23
[0]
[1]
[2]
One name holds many values. Each box has an index, and we count the index from 0 instead of 1.
int data[3] = {22, 24, 23};
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Example: three temperature readings in one array instead of three separate variables.

## Slide 7: Create an array: type, name, size.
7
Array
int data[6];
int array with a size of 6, without existing data
int value[5] = {2, 4, -8, 3, 2};
int array with a size of 5, with existing data
float number[2] = {2.8943, 10.23189};
You can use other data types too: float, size of 2
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 8: Write, read & clear by index.
8
Array
Write
int data[6] = {1,2,3,4,5,6};
data[1] = 10;
→ {1,10,3,4,5,6}
data[1] is the second element. To change the first, use [0].
Read
int data[6] = {1,10,3,4,5,6};
x = data[4];
→ x = 5
x gets a copy of the fifth element. The array does not change.
Clear
int data[6] = {1,10,3,4,5,6};
data[5] = 0;
→ {1,10,3,4,5,0}
We assume 0 means nothing, so this removes the sixth element.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 9: What would be the new array?
9
Checkpoint 2
READ THE CODE
int numbers[5] = {1,2,3,4,5};
numbers[2] = numbers[1] + numbers[4];
ANSWER
{1,2,7,4,5}
WHY
numbers[1] is 2 and numbers[4] is 5. Their sum, 7, replaces numbers[2], the third element.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 10: What will be printed?
10
Checkpoint 3
READ THE CODE
float data[8];
int x = 0;
data[2] = 1.23;
data[5] = 2.34;
data[7] = 3.45;
x = data[1] + data[5];
Serial.println(x);
ANSWER
2
WHY
data[1] was never set, so it is 0. 0 + 2.34 = 2.34, and x is an int, so the decimal part is dropped.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Answer: 2. This assumes data is declared above setup() (global), where unset elements start at 0. Declared inside a function, an unset element holds an unknown value, which is a good reason to always fill arrays before reading them.

## Slide 11: Repeat a command with a fixed structure.
11
For Loop
A for loop repeats some command. It is mainly used to control arrays.
for (int i = 0; i <= 25; i++)
{
Serial.println(i);
}
int i = 0
Initial value of a variable to control the loop
i <= 25
Used to determine the end of the loop
i++
Change of the value after each loop (i++ adds 1)
© 2026 Incipe Academy Limited. All rights reserved.
Notes: This prints 0, 1, 2 … up to 25, each on a new line: 26 lines in total.

## Slide 12: What will be printed?
12
Checkpoint 4
READ THE CODE
for (int i = 1; i < 10; i = i+2){
Serial.print(i);
}
ANSWER
13579
WHY
i starts at 1 and goes up by 2: 1, 3, 5, 7, 9. At 11 the loop stops. print keeps them on one line.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 13: Use i as the index.
13
For Loop + Array
int data[5] = {0,1,2,3,4};
void setup() {
Serial.begin(9600);
}
void loop() {
for (int i = 0; i < 5; i = i+1)
{
Serial.println(data[i]);
delay(1000);
}
}
i = 0
Initial value of i is 0, the first index
i < 5
Limit i to below 5, the size of the array
data[i]
Prints data[0] the 1st time, data[1] the 2nd time, and so on
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 14: What is the value of a?
14
Checkpoint 5
READ THE CODE
int a = 0;
int database[3] = {1,2,3};
for (int i = 1; i < 3; i++){
database[0] = database[0] + database[i];
}
a = database[0];
ANSWER
6
WHY
i = 1: 1 + 2 = 3. i = 2: 3 + 3 = 6. database[0] collects the total, so a is 6.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 15: Average & largest value of 100 readings.
15
For Loop + Array
AVERAGE
for (int i = 1; i < 100; i++){
database[0] = database[0] + database[i];
database[i] = 0;
}
float mean = database[0]/100;
Serial.println(mean);
Add every element into database[0], clearing each one, then divide by 100.
LARGEST VALUE
for (int i = 1; i < 100; i++){
if (database[0] < database[i]){
database[0] = database[i];
}
}
Serial.print(database[0]);
Whenever a bigger value turns up, keep it in database[0].
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Both assume float database[100] is already filled with readings, as in the Lesson 3 sound sensor sketch. Run one or the other: the average loop clears the array as it goes. The original slide had a typo (databse[0]) in the last line; it is corrected here.

## Slide 16: Handling data.
16
Classwork
YOUR NOTES
Refer to your note page 8.
YOU WILL NEED
An array to store the data, and a for loop to go through it.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 17: Three things to take away.
17
Recap
1
An array holds many values under one name; the index counts from 0.
2
A for loop has a start, an end condition and a step: for (int i = 0; i < 5; i++).
3
Together, data[i] inside a for loop reads every element: to print, total or find the largest.
Thank you!
© 2026 Incipe Academy Limited. All rights reserved.