## Slide 1: Session 8 Integration: The Smart Garden
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M3: Sensors & Modules
Notes: Session 8: calibrate the soil probe into % wet, automate watering with two thresholds, fail safe on a missing reading, and have AI suggest thresholds.

## Slide 2: Teach the board to look after a plant.
Lesson Overview
Part | Topic | Time
01 | The garden’s senses: three sensors at once | 6 min
02 | From a raw number to “% wet” | 7 min
03 | Practice: automatic watering with a gap | 10 min
04 | AI integration: design the logic, choose the thresholds | 7 min
Builds on calibrating the soil probe in Session 1, states from M2 Session 4, and if from Lesson 2.
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Students need the board, the soil moisture probe, the temperature and humidity sensor, the light sensor, a plant pot and a cup of water.

## Slide 3: Six words you will hear today.
Key Words
Word | Plain meaning
Calibrate | Measure your own sensor at two known points (bone dry, in water) so its numbers mean something.
Threshold | A number where the program changes what it does — below 30 % wet, start watering.
Hysteresis | Two thresholds, one to switch on and a higher one to switch off, so the output doesn’t flicker.
bool | A variable that is only ever true or false.
Fail-safe | When something goes wrong, fall back to the harmless choice — here, not watering.
Stand-in | A Serial.println in the spot where an actuator call will go.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: Hysteresis is the big idea of the session.

## Slide 4: A Smart Garden is a gardener’s morning round.
The Garden’s Senses
Feel the soil — dry? Water it. Look at the sky — dark? Switch on the lamp. Too hot? Open a window.
Each sensor answers one question; your program asks them all, every round.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: Integration means one program asking several sensors.

## Slide 5: Three questions the garden asks.
Meet the Sensors
ONE LINE OF CODE
float moisture = incipe.getSoilMoisture();
float temperature = incipe.getTemperature();
float light = incipe.getLightIntensity();
Call | Value | Not detected | Read it every
incipe.getSoilMoisture() | A float, a raw reading — no fixed unit | -1 | 500 ms
incipe.getTemperature() | A float in degrees Celsius (°C) | -1 | 2000 ms
incipe.getLightIntensity() | A float from 0 (dark) to 1023 (bright) | -1 | 20–500 ms
Don’t assume “high = wet”: calibrate your own soil probe. Wiki › Soil moisture, Temperature & humidity, Light.
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: These facts are copied from the Wiki pages and nothing more.

## Slide 6: Stand-ins mark where each actuator call will go.
The Actuators
Actuator | Job in the garden | Today’s stand-in
Water pump | Water the soil | PUMP ON / PUMP OFF
Servo | Open the greenhouse window | OPEN WINDOW / CLOSE WINDOW
LED strip | Grow light | GROW LIGHT ON / OFF
Their Wiki pages name the functions but don’t yet say what values they take. The logic is the hard part — and it’s all here.
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Each stand-in is a Serial.println where the actuator call will go once the Wiki pages are published.

## Slide 7: Two calibration readings turn any number into “% wet”.
From Raw to % Wet
Like a progress bar: at 30 MB of a 60 MB download you are half-way — 30 ÷ 60.
Here: how far from dry ÷ the whole way from dry to wet. Today’s code uses 100 (dry) and 40 (wet) as stand-ins — replace them with your Session 1 numbers.
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: The stand-ins also show that on some probes wet is the smaller number.

## Slide 8: Turn a raw reading into % wet.
Line by Line
1 const float DRY_VALUE = 100; // probe in air: change to yours
2 const float WET_VALUE = 40; // probe in water: change to yours
3
4 float wetPercent(float raw) {
5 return (raw - DRY_VALUE) / (WET_VALUE - DRY_VALUE) * 100;
6 }
LINE 1 · STEP 1 OF 6
Your reading with the probe in the air: bone dry.
VARIABLES
DRY_VALUE = 100
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: Step 1.

## Slide 9: Turn a raw reading into % wet.
Line by Line
1 const float DRY_VALUE = 100; // probe in air: change to yours
2 const float WET_VALUE = 40; // probe in water: change to yours
3
4 float wetPercent(float raw) {
5 return (raw - DRY_VALUE) / (WET_VALUE - DRY_VALUE) * 100;
6 }
LINE 2 · STEP 2 OF 6
Your reading with the probe in water: fully wet.
VARIABLES
DRY_VALUE = 100
WET_VALUE = 40
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Step 2.

## Slide 10: Turn a raw reading into % wet.
Line by Line
1 const float DRY_VALUE = 100; // probe in air: change to yours
2 const float WET_VALUE = 40; // probe in water: change to yours
3
4 float wetPercent(float raw) {
5 return (raw - DRY_VALUE) / (WET_VALUE - DRY_VALUE) * 100;
6 }
LINE 4 · STEP 3 OF 6
Call wetPercent(70): a reading between the two.
VARIABLES
DRY_VALUE = 100
WET_VALUE = 40
raw = 70
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: Step 3.

## Slide 11: Turn a raw reading into % wet.
Line by Line
1 const float DRY_VALUE = 100; // probe in air: change to yours
2 const float WET_VALUE = 40; // probe in water: change to yours
3
4 float wetPercent(float raw) {
5 return (raw - DRY_VALUE) / (WET_VALUE - DRY_VALUE) * 100;
6 }
LINE 5 · STEP 4 OF 6
How far from dry? 70 − 100 = −30.
VARIABLES
DRY_VALUE = 100
WET_VALUE = 40
raw = 70
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: Step 4.

## Slide 12: Turn a raw reading into % wet.
Line by Line
1 const float DRY_VALUE = 100; // probe in air: change to yours
2 const float WET_VALUE = 40; // probe in water: change to yours
3
4 float wetPercent(float raw) {
5 return (raw - DRY_VALUE) / (WET_VALUE - DRY_VALUE) * 100;
6 }
LINE 5 · STEP 5 OF 6
The whole way from dry to wet: 40 − 100 = −60.
VARIABLES
DRY_VALUE = 100
WET_VALUE = 40
raw = 70
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: Step 5.

## Slide 13: Turn a raw reading into % wet.
Line by Line
1 const float DRY_VALUE = 100; // probe in air: change to yours
2 const float WET_VALUE = 40; // probe in water: change to yours
3
4 float wetPercent(float raw) {
5 return (raw - DRY_VALUE) / (WET_VALUE - DRY_VALUE) * 100;
6 }
LINE 5 · STEP 6 OF 6
−30 ÷ −60 = 0.5, then × 100 = 50. Half-way to wet.
VARIABLES
DRY_VALUE = 100
WET_VALUE = 40
raw = 70
result = 50
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: If wet is the smaller number, both top and bottom are negative and the minus signs cancel.

## Slide 14: One threshold makes the pump flicker.
The Flicker Problem
“Water below 30 %”: at 30.1 % it stops, a minute later at 29.9 % it starts again — on, off, on, off.
Like running a bath: tap on when the water is low, off only when it is high enough. Two levels — that gap is hysteresis.
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Hysteresis: two thresholds, a gap between them.

## Slide 15: Two states, two thresholds.
Plan First
State | Switch when | Next state | Stand-in
Not watering | % wet below 30 | Watering | PUMP ON
Watering | % wet above 60 | Not watering | PUMP OFF
A two-state machine, like the traffic light in M2 Session 4. A bool remembers which state you’re in.
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: Same table-first habit as M2 Session 4.

## Slide 16: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 1 · STEP 1 OF 14
Start watering below 30 % wet.
VARIABLES
START = 30
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: Step 1.

## Slide 17: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 2 · STEP 2 OF 14
Stop only above 60 % wet.
VARIABLES
START = 30
STOP = 60
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: The gap between 30 and 60 stops the flicker.

## Slide 18: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 3 · STEP 3 OF 14
The pump starts off.
VARIABLES
watering = false
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: bool: only ever true or false.

## Slide 19: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 6 · STEP 4 OF 14
Round 1: the reading is 70.
VARIABLES
watering = false
raw = 70
wet = ?
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Step 4.

## Slide 20: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 8 · STEP 5 OF 14
Not −1, so convert: 50 % wet.
VARIABLES
watering = false
raw = 70
wet = 50
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: Lines 7 and 8 are the fail-safe: a -1 reading stays at 100 % wet.

## Slide 21: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 9 · STEP 6 OF 14
!watering means “not watering” — true. Is 50 below 30? No.
VARIABLES
watering = false
raw = 70
wet = 50
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: Step 6.

## Slide 22: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 10 · STEP 7 OF 14
Not watering, so this line does nothing either. Wait 2 s.
VARIABLES
watering = false
raw = 70
wet = 50
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: Step 7.

## Slide 23: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 8 · STEP 8 OF 14
Round 2: the reading is 85 — 25 % wet. The soil is drying.
VARIABLES
watering = false
raw = 85
wet = 25
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: Step 8.

## Slide 24: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 9 · STEP 9 OF 14
Not watering, and 25 is below 30: switch on.
VARIABLES
watering = true
raw = 85
wet = 25
SERIAL MONITOR
PUMP ON
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: Step 9.

## Slide 25: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 10 · STEP 10 OF 14
Is 25 above 60? No — keep going.
VARIABLES
watering = true
raw = 85
wet = 25
SERIAL MONITOR
PUMP ON
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: Step 10.

## Slide 26: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 8 · STEP 11 OF 14
Round 3: the reading is 73 — 45 % wet.
VARIABLES
watering = true
raw = 73
wet = 45
SERIAL MONITOR
PUMP ON
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Step 11.

## Slide 27: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 10 · STEP 12 OF 14
45 is above 30 now, but not above 60: the pump keeps running. That’s the gap at work.
VARIABLES
watering = true
raw = 73
wet = 45
SERIAL MONITOR
PUMP ON
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: This is hysteresis.

## Slide 28: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 8 · STEP 13 OF 14
Round 4: the reading is 61 — 65 % wet.
VARIABLES
watering = true
raw = 61
wet = 65
SERIAL MONITOR
PUMP ON
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: Step 13.

## Slide 29: Automatic watering, round by round.
Line by Line
1 const float START = 30; // % wet: start watering below this
2 const float STOP = 60; // % wet: stop watering above this
3 bool watering = false;
4
5 void loop() {
6 float raw = incipe.getSoilMoisture();
7 float wet = 100; // no reading: act as if wet
8 if (raw != -1) wet = wetPercent(raw);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 10 · STEP 14 OF 14
Watering, and 65 is above 60: switch off.
VARIABLES
watering = false
raw = 61
wet = 65
SERIAL MONITOR
PUMP ON
PUMP OFF
© 2026 Incipe Academy Limited. All rights reserved.
29
Notes: Put wetPercent() above loop(), add setup() with Serial.begin(9600), and Upload. Each PUMP line is where incipe.setPumpSpeed(speed) will go once the Wiki says what speed takes.

## Slide 30: Make it your garden.
Your Task
Step | Do this
1 | Put in your own calibration values. Pick START and STOP for a real plant.
2 | Grow light: print GROW LIGHT ON when the light falls below a threshold you choose (0 dark, 1023 bright), and OFF above a higher one. Use a second bool. Skip −1.
3 | Window: print OPEN WINDOW above 30 °C and CLOSE WINDOW below 27 °C.
4 | Pull the soil probe out while it runs. What does the Serial Monitor show, and why is that safe?
© 2026 Incipe Academy Limited. All rights reserved.
30
Notes: Step 4: the -1 reading keeps wet at 100, so nothing switches on.

## Slide 31: Ask the AI to design the logic and suggest thresholds.
AI Integration
PASTE YOUR SKETCH AND CALIBRATION INTO THE WORKSPACE AI CHAT WITH
I’m building a Smart Garden on an ESP32 board. My soil probe reads [DRY] in air and [WET] in water; I convert it to “% wet” with the function below. Suggest START and STOP thresholds for watering a [type of plant], and a light threshold for a grow lamp on a 0 (dark) to 1023 (bright) scale. Explain each number in one sentence for a beginner. Keep my hysteresis and my −1 fail-safe. Do not change any incipe.* call.
© 2026 Incipe Academy Limited. All rights reserved.
31
Notes: The curriculum task: use AI to design the automation logic and suggest optimal thresholds.

## Slide 32: Check what comes back like a reviewer.
AI Integration
Ask yourself | Why
Are its thresholds in % wet, not raw numbers? | The AI can’t know your probe’s raw range — only your calibration does.
Is STOP still higher than START? | Without the gap, the pump flickers again.
Is the −1 check still there? | A missing probe must never start the pump.
Did it invent pump, servo or LED code, or change an incipe.* call? | Never accept that — compare with the Wiki. Keep your stand-ins.
Does the plant advice make sense? | Ask it why — then check one fact yourself.
© 2026 Incipe Academy Limited. All rights reserved.
32
Notes: Treat the AI as a reviewer and adviser, not the author.

## Slide 33: With DRY 100 and WET 40, what does wetPercent(100) return?
Checkpoint 1
READ THE CODE
(100 - 100) / (40 - 100) * 100
ANSWER
0
WHY
The reading equals “dry”.
© 2026 Incipe Academy Limited. All rights reserved.
33
Notes: Answer: 0.

## Slide 34: And wetPercent(40)?
Checkpoint 2
READ THE CODE
(40 - 100) / (40 - 100) * 100
ANSWER
100
WHY
The reading equals “wet”.
© 2026 Incipe Academy Limited. All rights reserved.
34
Notes: Answer: 100.

## Slide 35: watering is false and the soil is 45 % wet. Does the pump start?
Checkpoint 3
READ THE CODE
if (!watering && wet < START)
...
// START = 30
ANSWER
No
WHY
45 is not below START (30), so line 9 does nothing.
© 2026 Incipe Academy Limited. All rights reserved.
35
Notes: Answer: no.

## Slide 36: watering is true and the soil is 45 % wet. What happens?
Checkpoint 4
READ THE CODE
if (watering && wet > STOP)
...
// STOP = 60
ANSWER
Keeps running
WHY
Same reading, different state, different result — that’s hysteresis.
© 2026 Incipe Academy Limited. All rights reserved.
36
Notes: Answer: the pump keeps running.

## Slide 37: If line 8 converted −1 anyway, what would wetPercent(-1) print?
Checkpoint 5
READ THE CODE
(-1 - 100) / (40 - 100) * 100
ANSWER
168.33
WHY
A nonsense “very wet”. A probe going the other way would give a nonsense “very dry” and start the pump.
© 2026 Incipe Academy Limited. All rights reserved.
37
Notes: Answer: 168.33.

## Slide 38: Three things to take away.
Recap
1
Calibrate, then convert: two readings turn any raw number into “% wet”, whichever way your probe goes.
2
Two thresholds — start low, stop high — and a bool for the state, so the pump switches once instead of flickering.
3
Fail safe: −1 never switches anything on. The AI can suggest thresholds; only your calibration knows your sensor.
Next — Session 9: Building the Game Console. Joystick, button and LED strip together.
© 2026 Incipe Academy Limited. All rights reserved.
38
Notes: Homework: finish the task, including the grow light and the window.