## Slide 1: Session 9 Integration: The Game Console
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M3: Sensors & Modules
Notes: M3 Session 9: the LED strip as a one-row screen, drawing each frame from the game state, and Strip Catcher on the Serial Monitor.

## Slide 2: Make a game on a one-row screen.
Lesson Overview
Part | Topic | Time
01 | A strip is a one-row screen | 6 min
02 | Drawing the game state | 8 min
03 | Practice: Strip Catcher — move, catch, score | 12 min
04 | Make it a console: restart, speed, and what’s coming | 4 min
Builds on joystick zones and edges from Session 5, the for loop from Lesson 4, and states from M2 Session 4.
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Students need the board, the joystick and the push button.

## Slide 3: Five words you will hear today.
Key Words
Word | Plain meaning
Pixel | One dot of light on the screen — on an LED strip, one LED.
Game state | Every number that describes the game right now: where you are, where the fruit is, the score.
Draw | Turn the game state into what the player sees.
constrain | Keeps a number inside a range: constrain(7, 0, 5) is 5.
% (remainder) | What’s left after dividing: 7 % 6 is 1. It wraps numbers around, like a clock.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: constrain is an Arduino function; % is plain C++.

## Slide 4: An LED strip is a screen one pixel tall.
A One-Row Screen
A stadium scoreboard is rows of bulbs; a strip is one row. Snake and Pong become one-row games: left or right.
Set pixels with incipe.setLEDcolour(...), push them out with incipe.showLED(). What setLEDcolour takes isn’t published yet — so today the Serial Monitor is the screen.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: The Wiki gives the two function names; their arguments are not published yet.

## Slide 5: One character per pixel, one line per frame.
Today’s Screen
On the strip | Today, on the Serial Monitor
Set one pixel’s colour | Print one character: P you, * the fruit, . off
incipe.showLED() — show the frame | Serial.println() — end the line
When the LED-strip page lists its arguments, only draw() changes. The game logic stays exactly the same.
The joystick is the controller: reuse zone() and your own limits from Session 5. The code still uses the stand-in limits 25 and 75.
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: Keeping logic and display apart is the big design idea.

## Slide 6: Each frame is a new page of a flip-book.
Drawing
You don’t move the drawing — you draw a new page from the facts: “you’re at 0, the fruit is at 4”.
The game state is three numbers. draw() visits every pixel with a for loop.
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Game state in, frame out.

## Slide 7: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 1 · STEP 1 OF 12
Our strip has 6 pixels, numbered 0 to 5.
VARIABLES
LEN = 6
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: Step 1.

## Slide 8: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 2 · STEP 2 OF 12
You start on pixel 0.
VARIABLES
LEN = 6
player = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: Step 2.

## Slide 9: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 3 · STEP 3 OF 12
The fruit waits on pixel 4.
VARIABLES
LEN = 6
player = 0
fruit = 4
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Step 3.

## Slide 10: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 4 · STEP 4 OF 12
No points yet.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: Lines 2 to 4 are the whole game state.

## Slide 11: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 7 · STEP 5 OF 12
Visit every pixel, starting at 0.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: Step 5.

## Slide 12: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 8 · STEP 6 OF 12
Pixel 0 is where you are: print P.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 0
SERIAL MONITOR
P
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: Step 6.

## Slide 13: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 7 · STEP 7 OF 12
Next pixel.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 1
SERIAL MONITOR
P
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: Step 7.

## Slide 14: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 10 · STEP 8 OF 12
Pixels 1, 2 and 3 are neither you nor the fruit: a dot each.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 3
SERIAL MONITOR
P...
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Step 8.

## Slide 15: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 9 · STEP 9 OF 12
Pixel 4 is the fruit: print *.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 4
SERIAL MONITOR
P...*
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: Step 9.

## Slide 16: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 10 · STEP 10 OF 12
Pixel 5: a dot. i becomes 6, not below 6, so the loop ends.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 5
SERIAL MONITOR
P...*.
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: Step 10.

## Slide 17: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 12 · STEP 11 OF 12
Then the score label…
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 5
SERIAL MONITOR
P...*. score
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: Step 11.

## Slide 18: Draw one frame.
Line by Line
1 const int LEN = 6; // pixels on our pretend strip
2 int player = 0; // where you are
3 int fruit = 4; // what you’re catching
4 int score = 0;
5
6 void draw() {
7 for (int i = 0; i < LEN; i++) {
8 if (i == player) Serial.print("P");
9 else if (i == fruit) Serial.print("*");
10 else Serial.print(".");
11 }
12 Serial.print(" score ");
13 Serial.println(score);
14 }
LINE 13 · STEP 12 OF 12
…and the score. println ends the frame.
VARIABLES
LEN = 6
player = 0
fruit = 4
score = 0
i = 5
SERIAL MONITOR
P...*. score 0
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: On the strip, this println becomes incipe.showLED().

## Slide 19: Strip Catcher: move, catch, score.
Practice
Event | What changes
Stick pushed (an edge) | player moves one pixel — but never off the strip
player lands on fruit | score goes up, fruit jumps 3 pixels on (wrapping round)
Anything changed | Draw a new frame
The curriculum task: map joystick inputs to game movements and display game state on LEDs.
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Plan the events first, then the code.

## Slide 20: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 4 · STEP 1 OF 10
Say you’re on pixel 3 and the fruit is on 4. You push right: zone 1.
VARIABLES
player = 3
fruit = 4
score = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: Step 1.

## Slide 21: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 5 · STEP 2 OF 10
Just pushed (it was resting last pass) — go in.
VARIABLES
player = 3
fruit = 4
score = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: Step 2.

## Slide 22: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 3 OF 10
3 + 1 = 4, inside 0 to 5, so you move to pixel 4.
VARIABLES
player = 4
fruit = 4
score = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: constrain(value, low, high) keeps value between low and high.

## Slide 23: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 7 · STEP 4 OF 10
You’re on the fruit!
VARIABLES
player = 4
fruit = 4
score = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: Step 4.

## Slide 24: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 8 · STEP 5 OF 10
score++ adds 1 to the score.
VARIABLES
player = 4
fruit = 4
score = 1
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: Step 5.

## Slide 25: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 9 · STEP 6 OF 10
(4 + 3) is 7, and 7 % 6 is 1: the next fruit is on pixel 1.
VARIABLES
player = 4
fruit = 1
score = 1
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: % is the remainder after dividing. It wraps the fruit back to the start.

## Slide 26: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 11 · STEP 7 OF 10
Draw the new frame.
VARIABLES
player = 4
fruit = 1
score = 1
z = 1
SERIAL MONITOR
.*..P. score 1
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Step 7.

## Slide 27: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 13 · STEP 8 OF 10
Remember: pushed. Holding the stick won’t move you again.
VARIABLES
player = 4
fruit = 1
score = 1
z = 1
lastZone = 1
SERIAL MONITOR
.*..P. score 1
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: Step 8.

## Slide 28: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 9 OF 10
Later you’re on pixel 5 and push right again: 5 + 1 = 6 — but constrain keeps you at 5.
VARIABLES
player = 5
fruit = 1
score = 1
z = 1
lastZone = 0
SERIAL MONITOR
.*..P. score 1
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: Step 9.

## Slide 29: The game loop, one push at a time.
Line by Line
1 int lastZone = 0;
2
3 void loop() {
4 int z = zone(incipe.getJoystickXMovement()); // from Session 5
5 if (z != 0 && lastZone == 0) { // just pushed
6 player = constrain(player + z, 0, LEN - 1); // stay on the strip
7 if (player == fruit) { // caught it!
8 score++;
9 fruit = (fruit + 3) % LEN; // next fruit, 3 pixels on
10 }
11 draw();
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 11 · STEP 10 OF 10
Draw: you’re stuck against the end wall.
VARIABLES
player = 5
fruit = 1
score = 1
z = 1
lastZone = 0
SERIAL MONITOR
.*..P. score 1
.*...P score 1
© 2026 Incipe Academy Limited. All rights reserved.
29
Notes: Put zone() and draw() above loop(), call draw() once in setup() after Serial.begin(9600), and Upload.

## Slide 30: A console has a restart button.
Make It a Console
ONE LINE OF CODE
float pressed = incipe.getButtonResponse();
Button | You get
Pressed | 1
Not pressed | 0
Not detected | -1
Restart on release, exactly like selecting a menu item in Session 5. The IR remote joins once Session 7 can be written — its functions are not on the Wiki yet.
© 2026 Incipe Academy Limited. All rights reserved.
30
Notes: Copied from the Button page of the Wiki.

## Slide 31: Make it a real game.
Your Task
Step | Do this
1 | Build Strip Catcher with your own joystick limits. Catch three fruits.
2 | Restart: when the push button is released, reset player, fruit and score and draw a frame.
3 | After 20 moves print GAME OVER and your score. Which state variable do you need to add?
4 | Change LEN to 10 and the jump to (fruit + 7) % LEN. Trace the first three fruit positions by hand, then check.
© 2026 Incipe Academy Limited. All rights reserved.
31
Notes: Step 4 from fruit 4 with LEN 10: 1, then 8, then 5.

## Slide 32: LEN 6, player 0, fruit 4, score 0. What does draw() print?
Checkpoint 1
READ THE CODE
for (int i = 0; i < LEN; i++) {
if (i == player) Serial.print("P");
else if (i == fruit) Serial.print("*");
else Serial.print(".");
}
ANSWER
P...*. score 0
WHY
P on pixel 0, dots on 1–3, * on 4, a dot on 5, then the score.
© 2026 Incipe Academy Limited. All rights reserved.
32
Notes: Answer: P...*. score 0.

## Slide 33: You’re on pixel 0 and push left (zone −1). Where are you now?
Checkpoint 2
READ THE CODE
player = constrain(player + z, 0, LEN - 1);
ANSWER
0
WHY
0 + (−1) is −1, and constrain(-1, 0, 5) keeps it at 0.
© 2026 Incipe Academy Limited. All rights reserved.
33
Notes: Answer: pixel 0.

## Slide 34: You catch the fruit on pixel 4. Where is the next fruit?
Checkpoint 3
READ THE CODE
fruit = (fruit + 3) % LEN;
// LEN = 6
ANSWER
1
WHY
(4 + 3) % 6 = 7 % 6 = 1.
© 2026 Incipe Academy Limited. All rights reserved.
34
Notes: Answer: pixel 1.

## Slide 35: And if you caught it on pixel 5?
Checkpoint 4
READ THE CODE
fruit = (fruit + 3) % LEN;
// LEN = 6
ANSWER
2
WHY
(5 + 3) % 6 = 8 % 6 = 2.
© 2026 Incipe Academy Limited. All rights reserved.
35
Notes: Answer: pixel 2.

## Slide 36: From pixel 0 you hold the stick right for 20 passes. Where are you?
Checkpoint 5
READ THE CODE
if (z != 0 && lastZone == 0) {
player = ...
}
lastZone = z;
ANSWER
1
WHY
Only the first pass is an edge, so you move once.
© 2026 Incipe Academy Limited. All rights reserved.
36
Notes: Answer: pixel 1.

## Slide 37: Three things to take away.
Recap
1
An LED strip is a one-row screen: draw a frame from the game state by visiting every pixel with a for loop.
2
The joystick’s edge moves you one pixel per push; constrain keeps you on the strip and % wraps the fruit around.
3
Keep game logic apart from the display: only draw() changes when the strip’s calls are published.
Next — Session 10: System integration & debugging. Testing the Smart Garden and the Game Console end to end, and finding bugs with Serial prints and AI.
© 2026 Incipe Academy Limited. All rights reserved.
37
Notes: Homework: finish the task, including GAME OVER after 20 moves.