## Slide 1: Session 10 System Integration & Debugging
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M3: Sensors & Modules
Notes: M3 Session 10: debugging like a detective, labelled Serial prints that find a real bug, a full test plan for both projects, and AI edge cases checked on the board.

## Slide 2: Find out why it doesn’t work — then prove that it does.
Lesson Overview
Part | Topic | Time
01 | Debugging like a detective | 7 min
02 | Serial prints: make the invisible visible | 9 min
03 | Practice: a full system test of both projects | 9 min
04 | AI integration: edge cases and robustness | 5 min
Builds on everything in M3 — especially the −1 fail-safe from Session 8 and the joystick edge from Session 5.
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Students need the Smart Garden and Game Console builds from Sessions 8 and 9.

## Slide 3: Six words you will hear today.
Key Words
Word | Plain meaning
Bug | A mistake that makes a program do something you didn’t mean.
Debugging | Finding the bug and fixing it.
Symptom | What you see go wrong — “the pump never starts”. Not the cause.
Hypothesis | Your best guess at the cause, which a test can prove or disprove.
Edge case | An unusual situation at the limits: a sensor unplugged, a button held, the end of the strip.
Test plan | A table of things to try, what should happen, and what did happen.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: Symptom versus cause is the key distinction.

## Slide 4: Debug like a doctor, not a guesser.
Debugging
A patient says “my head hurts” — the symptom. The doctor forms a hypothesis, runs a test, and only then treats.
Never change code at random. Every change is a test of one idea.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: Debugging is the scientific method applied to code.

## Slide 5: Five steps, every time.
The Method
Step | Ask yourself
1. Symptom | What exactly goes wrong? When? Every time?
2. Clue | What do the numbers inside the program say? (Serial prints.)
3. Hypothesis | Which line could cause this?
4. Test | Change one thing, run it again. Did the symptom change?
5. Fix and retest | Fix it, then rerun every test that used to pass.
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: Step 5 matters: a fix can break something that used to work.

## Slide 6: Add one module at a time.
Integration
When the Smart Garden “doesn’t work”, which part is broken — the probe, the conversion, the thresholds?
Add one module, test it, then add the next. If it breaks, the bug is in what you just added.
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Incremental integration keeps the search small.

## Slide 7: Make the invisible visible.
Serial Prints
The board can’t show you its variables — unless you print them, with a label.
Next: the Smart Garden with one small change and a bug. The soil is bone dry, but the pump never starts.
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: A debug print compares what the program thinks with what is really happening.

## Slide 8: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 2 · STEP 1 OF 8
The probe is in dry soil. The sensor gives 85.
VARIABLES
raw = 85
watering = false
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: Step 1.

## Slide 9: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 3 · STEP 2 OF 8
85 converts to 25 % wet — dry, as expected.
VARIABLES
raw = 85
watering = false
wet = 25
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Step 2.

## Slide 10: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 4 · STEP 3 OF 8
Look closely: = not ==. This line puts −1 into raw.
VARIABLES
raw = -1
watering = false
wet = 25
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: = sets a value; == compares.

## Slide 11: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 4 · STEP 4 OF 8
The if sees −1, which isn’t 0, so it counts as true: wet becomes 100.
VARIABLES
raw = -1
watering = false
wet = 100
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: Step 4.

## Slide 12: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 6 · STEP 5 OF 8
The debug print shows what the program now believes.
VARIABLES
raw = -1
watering = false
wet = 100
SERIAL MONITOR
[debug] raw=-1.00
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: Step 5.

## Slide 13: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 8 · STEP 6 OF 8
…and the soil looks soaking wet.
VARIABLES
raw = -1
watering = false
wet = 100
SERIAL MONITOR
[debug] raw=-1.00 wet=100.00
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: Step 6.

## Slide 14: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 9 · STEP 7 OF 8
100 is not below 30, so the pump never starts. That’s the symptom.
VARIABLES
raw = -1
watering = false
wet = 100
SERIAL MONITOR
[debug] raw=-1.00 wet=100.00
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Step 7.

## Slide 15: Find the bug with debug prints.
Line by Line
1 void loop() {
2 float raw = incipe.getSoilMoisture();
3 float wet = wetPercent(raw);
4 if (raw = -1) wet = 100; // meant: no reading → act as if wet
5 Serial.print("[debug] raw=");
6 Serial.print(raw);
7 Serial.print(" wet=");
8 Serial.println(wet);
9 if (!watering && wet < START) { watering = true; Serial.println("PUMP ON"); }
10 if (watering && wet > STOP) { watering = false; Serial.println("PUMP OFF"); }
11 delay(2000);
12 }
LINE 4 · STEP 8 OF 8
The clue: the sensor said 85, the print says −1. Line 4 changed raw. Fix: raw == -1.
VARIABLES
raw = -1
watering = false
wet = 100
SERIAL MONITOR
[debug] raw=-1.00 wet=100.00
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: The bug sits between the last right value and the first wrong one.

## Slide 16: The compiler may stay silent.
Read the Warnings
THE FIX
if (raw == -1) wet = 100;
With all warnings switched on, the compiler says “suggest parentheses around assignment used as truth value”.
With the default settings, the same code compiles without a word — so never count on a warning to catch it.
Fixed, a reading of 85 prints [debug] raw=85.00 wet=25.00, then PUMP ON.
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: We compiled both versions: the warning appears only with all warnings on.

## Slide 17: Four habits.
Good Debug Prints
Do | Why
Label every value: raw=, wet= | A bare 85 on the screen means nothing two minutes later.
Print before and after a suspect line | The bug is between the last right value and the first wrong one.
Print the state too: watering=1 | Many bugs are “the program thinks it’s in a different state”.
Remove or switch them off when done | Extra prints slow the loop and hide real output.
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: Try it: put the buggy line into your Smart Garden, watch the debug lines, then fix it.

## Slide 18: A logic analyzer records signals over time.
Logic Analyzers
Engineers use one to see two chips talking bit by bit, when a wired connection misbehaves.
For incipe.* code the board handles that conversation for you, so Serial prints are your first and best tool.
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: The curriculum names logic analyzers; this is the concept only.

## Slide 19: Smart Garden test plan.
Practice · Full System Test
# | Do this | Expected | Actual | Pass?
1 | Probe in the air, with a debug print of wet | wet close to 0; PUMP ON once |  | 
2 | Then probe into a cup of water | wet close to 100; PUMP OFF once |  | 
3 | Damp soil between your thresholds | No new PUMP line — the state is kept |  | 
4 | Unplug the probe while the pump is off | Nothing switches on |  | 
5 | Unplug the probe while the pump is on | PUMP OFF on the next round |  | 
6 | Cover the light sensor (grow-light task) | GROW LIGHT ON once |  | 
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Expected results come from the Session 8 code. Fill in Actual and Pass on the board.

## Slide 20: Game Console test plan.
Practice · Full System Test
# | Do this | Expected | Actual | Pass?
1 | Leave the stick alone | No new frames |  | 
2 | Push right and hold for 5 s | One frame, you moved one pixel |  | 
3 | On pixel 0, push left | You stay on pixel 0 |  | 
4 | Catch the fruit on pixel 4 | score 1, the next fruit on pixel 1 |  | 
5 | Unplug the joystick | Nothing moves — zone(-1) is 0 |  | 
6 | Hold the push button 3 s, then let go (restart task) | One restart, not several |  | 
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: When a row fails: symptom, clue, hypothesis, one change, retest — then rerun the whole table.

## Slide 21: Ask the AI to predict edge cases.
AI Integration
PASTE ONE PROJECT’S SKETCH INTO THE WORKSPACE AI CHAT WITH
Here is my Smart Garden sketch for an ESP32 board. List 6 edge cases it might meet (missing sensors, odd readings, timing). For each, predict exactly what my code prints, and suggest one robustness improvement in one sentence for a beginner. Do not rewrite the program, and do not change or add any incipe.* calls.
The AI can’t run your board — it predicts. Your job is to check.
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: The curriculum task: use AI to simulate edge cases and suggest robustness improvements.

## Slide 22: Check every prediction on the board.
AI Integration
Ask yourself | Why
Can I test each edge case on the board? | Add the testable ones as new rows in your test plan.
Did the prediction match what really printed? | Mark every row where the AI was wrong.
Does each suggestion keep the −1 fail-safe and the hysteresis? | “Robust” must never mean the pump runs when it shouldn’t.
Did it invent incipe.* functions or arguments? | Never accept that — compare with the Wiki.
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: Treat the AI as a source of ideas to test, not of answers.

## Slide 23: Buggy code, the sensor gives 85. What does the debug line print?
Checkpoint 1
READ THE CODE
if (raw = -1) wet = 100;
Serial.print("[debug] raw=");
Serial.print(raw);
Serial.print(" wet=");
Serial.println(wet);
ANSWER
raw=-1.00 wet=100.00
WHY
Line 4 sets raw to −1 and wet to 100 before the print. (The line starts with [debug].)
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: Answer: [debug] raw=-1.00 wet=100.00.

## Slide 24: Fixed to ==, the sensor gives 85, watering is false. What prints?
Checkpoint 2
READ THE CODE
if (raw == -1) wet = 100;
...
if (!watering && wet < START) ...
ANSWER
raw=85.00 wet=25.00, PUMP ON
WHY
The debug line, then PUMP ON — 25 is below START (30).
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: Answer: [debug] raw=85.00 wet=25.00, then PUMP ON.

## Slide 25: Fixed, the probe is unplugged (−1). What does the debug line print?
Checkpoint 3
READ THE CODE
if (raw == -1) wet = 100;
ANSWER
raw=-1.00 wet=100.00
WHY
Exactly what the bug printed! A print alone can’t tell “unplugged” from “bug” — plug the probe into dry soil and see whether raw changes.
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: Answer: the same line as the bug.

## Slide 26: Fixed, watering is true, the probe is unplugged. What prints next?
Checkpoint 4
READ THE CODE
if (watering && wet > STOP)
... Serial.println("PUMP OFF");
ANSWER
PUMP OFF
WHY
A −1 reading keeps wet at 100, above STOP (60). The fail-safe switches the pump off.
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Answer: PUMP OFF.

## Slide 27: Game Console: you’re on pixel 5 of 6 and push right. What should the test plan say?
Checkpoint 5
READ THE CODE
player = constrain(player + z, 0, LEN - 1);
ANSWER
Stay on 5
WHY
constrain(6, 0, 5) is 5.
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: Answer: you stay on pixel 5.

## Slide 28: Three things to take away.
Recap
1
Debug like a detective: symptom, clue, hypothesis, change one thing, retest — and integrate one module at a time.
2
Labelled Serial prints show what the program believes; watch for = where you meant ==.
3
A test plan with expected results turns “it seems to work” into proof; the AI suggests edge cases, the board confirms them.
Next — M4 Session 1: Design thinking & problem statement. From building things right to building the right thing.
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: Homework: complete both test plans and fix every failing row.