## Slide 1: Session 2 AI-Powered Firmware Development
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M1: AI Literacy
Notes: Session 2 of M1 AI Literacy. Today the Workspace AI writes the first draft of a function for the temperature and humidity sensor, and we learn to review it and make it use less memory. Thirty minutes, five parts.

## Slide 2: Let the AI write the first draft. You review it, check it and make it smaller.
Lesson Overview
Part | Topic | Time
01 | From a sentence to firmware in INCIPE Workspace | 6 min
02 | Reviewing what the AI wrote | 8 min
03 | Making it smaller: memory | 8 min
04 | When to trust AI, and when to write it yourself | 4 min
05 | Practice: the climate reader | 4 min + homework
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Five parts in thirty minutes. The big idea: the AI is fast at drafts, you are responsible for checking them. The practice task at the end continues as homework.

## Slide 3: Seven words you will hear today.
Key Words
Word | Plain meaning
Firmware | The program that runs on the board itself, not on your computer.
Compile | Translate the code you can read into instructions the board can run.
Function | A named block of code that does one job. You call it by its name.
Variable | A labelled box that holds one value, like temperature.
Memory (RAM) | The board's short-term workspace, where variables live while the program runs. It is small.
Byte | The unit memory is counted in. One letter of text takes about one byte.
Code review | Reading code line by line to find mistakes before it runs.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: Read these aloud once. Students only need the plain meaning today; M2 Session 1 goes deeper into memory, RAM and Flash.

## Slide 4: Describe, draft, verify, upload.
From a Sentence to Firmware
Describe
The AI chat
Say what the board should do, in one or two sentences.
Draft
The code editor
The AI writes the firmware into your project.
Verify
Top bar
Compiles your code and reports the first mistake it finds.
Upload
Next to Verify
Compiles and sends the code to the selected board. Read it in the Console.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: Think of the Workspace AI as a new lab partner who types very fast. They have never seen your board before, so you still check their work. Two of these four steps are yours: describing clearly, and checking what comes back. Connecting the board and the Console are covered in the Wiki page Connect the board.

## Slide 5: Describe it in the chat, then Verify and Upload.
INCIPE Workspace
The AI chat. Today's prompt: read the DHT11, print both values every 2 seconds, and print a short message if a reading is −1.
The top bar, left to right: Verify, Upload, the Board menu, then the Code editor, Artifacts, Skills and Console panels.
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: Real screenshots of the current Workspace. Type the prompt into the chat and send it. When the draft appears, Verify first. Upload only after Verify passes, then open the Console to read what the board prints.

## Slide 6: Compiles is not the same as correct.
The One Rule
The Workspace AI builds with Incipe's own toolchain, so its code either compiles or it does not. That catches spelling and grammar mistakes in the code. It cannot tell whether the code does what you meant.
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Pause here. Checking that the code does what you meant is your job, and it is the rest of this lesson.

## Slide 7: One line of code for each value.
Temperature & Humidity Sensor
ONE LINE OF CODE
float temperature = incipe.getTemperature();
float humidity = incipe.getHumidity();
What you get | incipe.getTemperature() | incipe.getHumidity()
Value | A float in degrees Celsius (°C) | A float, % relative humidity, 0–100
Not detected | -1 | -1
Read it every | 2000 ms | 2000 ms
A float is a number with a decimal point, like 23.4. Full details: Wiki › Temperature & humidity sensor.
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: The DHT11 is a slow sensor: reading it more often than every 1 to 2 seconds does not give fresher data. Minus one means the sensor is not detected yet. These facts are exactly what the Wiki page says, nothing more.

## Slide 8: A typical first draft. It compiles, and it works — sometimes.
Reviewing the AI's Draft
AI DRAFT
1 String readClimate() {
2 double temperature = incipe.getTemperature();
3 double humidity = incipe.getHumidity();
4 String report = "Temperature: " + String(temperature) + " C, Humidity: " + String(humidity) + " %";
5 return report;
6 }
Line | What it does
1 | Starts a function called readClimate that hands back a String (a piece of text).
2–3 | Asks the sensor for each value and keeps it in a double box.
4 | Glues words and both numbers into one long piece of text called report.
5–6 | Hands that text back to whoever called the function, and ends it.
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: This is the kind of draft an AI often gives for "write a function that reads the temperature and humidity". It compiles, and it even works when the sensor is plugged in. Ask the class what could go wrong before showing the next slide.

## Slide 9: Review the draft before you trust it.
Five Questions for Every Draft
# | Ask | This draft
1 | Does every incipe.* name match the Wiki exactly? | Yes — getTemperature(), getHumidity()
2 | Does it handle −1 (sensor not detected)? | No. It would print Temperature: -1.00 C as if it were real.
3 | Do the types match what the function returns? | No. The Wiki says float; the draft uses double.
4 | Does it read at the right speed? | Not decided here — we will run it every 2000 ms.
5 | Does it keep anything it does not need? | Yes — the whole sentence is stored as text first.
A wrong name is the easiest mistake: Verify stops at it. The −1 mistake and the memory waste both compile without a complaint — only a human review finds them.
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Go through the five questions one by one. If the AI had written incipe.readTemperature(), Verify would stop at that line because no such function exists. The other two problems are invisible to the compiler.

## Slide 10: A float takes a 4-byte locker. A double takes 8.
Making It Smaller
The board's memory is a short row of lockers. A double holds extra decimal places — but the sensor only ever hands us a float, so the extra space holds nothing.
A String is a stretchy bag: every time you glue more words on, it asks for a new, bigger space and copies everything across. Every two seconds, on a small board, that wastes memory.
Item | AI draft | Optimised
Temperature | double — 8 bytes | float — 4 bytes
Humidity | double — 8 bytes | float — 4 bytes
The sentence | Built as one String every call | Not stored — printed piece by piece
Sizes for the INCIPE Board's ESP32: float 4 bytes, double 8 bytes.
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: Two lockers of 8 bytes become two lockers of 4 bytes: 8 bytes saved, every time the function runs. Building the String every two seconds can also leave memory in scattered pieces. Next: the optimised version, one line at a time.

## Slide 11: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 1 · STEP 1 OF 10
void means the function hands nothing back — it prints instead of returning text.
VARIABLES
None yet.
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: Step 1 of 10. Same output as the AI draft, less memory, and it handles minus one. We follow one call where the sensor gives 23.4 degrees and 51 percent. void means the function gives nothing back; it prints instead.

## Slide 12: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 2 · STEP 2 OF 10
Ask the sensor for the temperature. Say it is 23.4 °C. A float is all we need.
VARIABLES
temperature = 23.4
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: Step 2. The sensor hands back a float, so the box is a float: 4 bytes, not 8.

## Slide 13: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 3 · STEP 3 OF 10
Ask for the humidity: 51 %. Another 4-byte float.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: Step 3. Two floats: 8 bytes in total, where the AI draft used 16.

## Slide 14: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 4 · STEP 4 OF 10
|| means "or". Is either value −1? Neither is, so we skip lines 5 and 6.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Step 4. This is the minus-one check the AI draft forgot. If either value were minus one, line 5 would print a short message and line 6, return, would leave the function before any fake numbers are printed.

## Slide 15: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 8 · STEP 5 OF 10
Print the label. print stays on the same line.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
Temperature:
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: Step 5. We jumped from line 4 to line 8 because the if was false. Instead of building one long String, the sentence is printed one piece at a time, so nothing is stored.

## Slide 16: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 9 · STEP 6 OF 10
Print the number. Arduino prints a float with two decimal places: 23.40.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
Temperature: 23.40
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: Step 6. Serial.print of a float shows two decimal places by default, so 23.4 appears as 23.40.

## Slide 17: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 10 · STEP 7 OF 10
More label text, still on the same line.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
Temperature: 23.40 C, Humidity:
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: Step 7. Still print, not println, so the text keeps going on the same line.

## Slide 18: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 11 · STEP 8 OF 10
Print the humidity, also with two decimals: 51.00.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
Temperature: 23.40 C, Humidity: 51.00
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: Step 8. The humidity float, 51, prints as 51.00.

## Slide 19: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 12 · STEP 9 OF 10
println adds the last piece and then starts a new line.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
Temperature: 23.40 C, Humidity: 51.00 %
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Step 9. The finished line: Temperature: 23.40 C, Humidity: 51.00 %. Exactly what the AI draft printed, without storing a String.

## Slide 20: The optimised printClimate().
Line by Line
1 void printClimate() {
2 float temperature = incipe.getTemperature();
3 float humidity = incipe.getHumidity();
4 if (temperature == -1 || humidity == -1) {
5 Serial.println("DHT11 not detected yet");
6 return;
7 }
8 Serial.print("Temperature: ");
9 Serial.print(temperature);
10 Serial.print(" C, Humidity: ");
11 Serial.print(humidity);
12 Serial.println(" %");
13 }
LINE 13 · STEP 10 OF 10
The function ends. Next call, it reads fresh values. Run it every 2000 ms from a user thread.
VARIABLES
temperature = 23.4
humidity = 51.0
SERIAL MONITOR
Temperature: 23.40 C, Humidity: 51.00 %
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: Step 10. To run it every 2 seconds, ask the AI to call printClimate from a user thread paced at 2000 milliseconds, the speed the Wiki gives for the DHT11. M3 Session 1 explains threads in full.

## Slide 21: Trust it to multiply. Check that you typed the right numbers.
When to Trust AI
Trust the AI to… | Check it yourself when… | Write it yourself when…
Write a first draft fast | It uses an incipe.* name — compare it with the Wiki | You cannot explain what a line does yet
Explain an error message | It reads a sensor — is −1 handled? | The fix is one or two lines
Suggest a review checklist | It picks a type or a timing — does it match the Wiki? | You are learning that idea for the first time
Draft comments and a README | It builds text or keeps lists of values | Safety matters: anything that moves or gets hot
Reusable prompt: Review this function line by line. List anything that wastes memory and anything that breaks if the sensor returns −1. Do not rewrite it.
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: A calculator analogy: you trust it to multiply, but you still check you typed the right numbers. A second prompt worth keeping: explain what each line of this function does, in one short sentence per line, for a beginner.

## Slide 22: Prompt, verify, review, fix by hand, upload.
Try It
Open a new project in INCIPE Workspace and send today's prompt.
Click Verify. If it fails, ask the AI: "Explain this error in one sentence. Do not rewrite the code."
Review the draft with the five questions. Write down every "No".
Fix them by hand: double to float, add the −1 check, print instead of building a String.
Verify again, then Upload and watch the Console. Unplug the sensor: you should see DHT11 not detected yet.
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: Ten minutes in class. Walk round and check that students make the fixes themselves rather than asking the AI to rewrite. Step 5 proves the minus-one check works.

## Slide 23: Generate it with AI, then optimise the memory by hand.
Practice: The Climate Reader
Step | Do this | Hand in
1 | Prompt the Workspace AI for a temperature & humidity read function, using Role, Goal, Context from Lesson 1. | Your prompt
2 | Copy the AI's first draft, unchanged. | Draft A
3 | Mark every line that uses more memory than it needs, and say why in one sentence. | Your notes
4 | Rewrite it by hand so it uses float, stores no String, and handles −1. | Draft B
5 | Fill in the table: bytes used by the variables in Draft A vs Draft B. | The table
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: This is the curriculum's practice task: use AI to generate a function that reads from the temperature and humidity sensor, then manually optimise the memory usage. Five deliverables.

## Slide 24: Temperature is 23.4 and humidity is −1. What prints?
Checkpoint 1
READ THE CODE
float temperature = incipe.getTemperature();
float humidity = incipe.getHumidity();
if (temperature == -1 || humidity == -1) {
Serial.println("DHT11 not detected yet");
return;
}
Serial.print("Temperature: ");
…
ANSWER
DHT11 not detected yet
WHY
23.4 is fine, but humidity is −1, so the "or" test is true. The function prints the message and returns before any numbers.
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: Answer: DHT11 not detected yet. Only one of the two values has to be minus one for the or test to be true.

## Slide 25: Temperature is 18 and humidity is 60. What prints?
Checkpoint 2
READ THE CODE
Serial.print("Temperature: ");
Serial.print(temperature);
Serial.print(" C, Humidity: ");
Serial.print(humidity);
Serial.println(" %");
ANSWER
Temperature: 18.00 C, Humidity: 60.00 %
WHY
Neither value is −1, so the whole line prints. Arduino prints each float with two decimal places.
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: Answer: Temperature: 18.00 C, Humidity: 60.00 %. The two decimal places come from how Arduino prints a float.

## Slide 26: Two doubles become two floats. How many bytes are saved?
Checkpoint 3
READ THE CODE
// AI draft
double temperature = incipe.getTemperature();
double humidity = incipe.getHumidity();
// Optimised
float temperature = incipe.getTemperature();
float humidity = incipe.getHumidity();
ANSWER
8 bytes
WHY
Two doubles = 2 × 8 = 16 bytes. Two floats = 2 × 4 = 8 bytes. 16 − 8 = 8.
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Answer: 8 bytes. On the INCIPE Board's ESP32 a double is 8 bytes and a float is 4.

## Slide 27: The AI wrote this line. What happens when you click Verify?
Checkpoint 4
READ THE CODE
float t = incipe.readTemperature();
ANSWER
Verify stops with an error at that line
WHY
There is no readTemperature(). The Wiki's name is incipe.getTemperature(), and names must match exactly.
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: Answer: Verify stops with an error. Verify compiles the code and reports the first mistake it finds; a function name that does not exist is exactly that kind of mistake.

## Slide 28: A classmate reads the DHT11 every 500 ms "for fresher data". Right?
Checkpoint 5
READ THE CODE
printClimate();
vTaskDelay(pdMS_TO_TICKS(500));
ANSWER
No — read it every 2000 ms
WHY
The Wiki says the DHT11 is a slow sensor: reading it more often than every 1–2 seconds does not give fresher data. It only prints the same values more often.
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: Answer: No. The Wiki's read interval for the DHT11 is 2000 milliseconds. M3 Session 1 covers threads and vTaskDelay in full.

## Slide 29: Three things to take away.
Recap
1
The Workspace AI turns a sentence into firmware that compiles. Compiling is not the same as correct.
2
Review every draft: exact incipe.* names, the −1 rule, types and timing from the Wiki, and nothing stored that is not needed.
3
Match the type to the data — float, not double — and print instead of building Strings. Same output, less memory.
Next — Session 3: Terminal commands & environment setup. ls, cd, mkdir and friends, and your first look at Git.
© 2026 Incipe Academy Limited. All rights reserved.
29
Notes: Three points to remember. Homework: finish the climate reader practice table. Next session moves to the terminal.