## Slide 1: Session 4 Structs & State Machines
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M2: Programming with C++
Notes: Session 4: group related values with struct, plan a state machine as a table, and build the curriculum's traffic light. Then AI reviews the logic.

## Slide 2: Keep related values together, and give your program a clear set of moods.
Lesson Overview
Part | Topic | Time
01 | struct: one card for related values | 8 min
02 | State machines: one state at a time | 8 min
03 | Practice: a traffic light | 9 min
04 | AI integration: review your state machine | 5 min
Builds on functions and switch from Session 2, and the sensor readings from Lesson 3.
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Four parts in thirty minutes. Students need the board, the temperature and humidity sensor and the light sensor.

## Slide 3: Six words you will hear today.
Key Words
Word | Plain meaning
struct | A new type you design yourself, that groups several values under one name.
Member | One value inside a struct, reached with a dot: d.temperature.
State | What the program is doing right now — like "red" for a traffic light.
Transition | Moving from one state to the next.
State machine (FSM) | A program that is always in exactly one state and moves between states by clear rules.
enum | A list of named values, like RED, YELLOW, GREEN, so code says names instead of numbers.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: FSM stands for finite state machine: finite because the list of states is fixed.

## Slide 4: A struct is a student ID card for your data.
struct
Name, class and number belong together, so they are printed on one card — not on three loose slips of paper.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: Our card will hold three sensor readings that belong together: temperature, humidity and light.

## Slide 5: Three readings that belong together.
Meet the Sensors
ONE LINE OF CODE
float temperature = incipe.getTemperature();
float humidity = incipe.getHumidity();
float light = incipe.getLightIntensity();
Call | Value | Not detected | Read it every
incipe.getTemperature() | A float in degrees Celsius (°C) | -1 | 2000 ms
incipe.getHumidity() | A float, % relative humidity, 0–100 | -1 | 2000 ms
incipe.getLightIntensity() | A float from 0 (dark) to 1023 (bright) | -1 | 20–500 ms
Full details: Wiki › Temperature & humidity sensor, Wiki › Light sensor.
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: These facts are copied from the Wiki pages and nothing more.

## Slide 6: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 1 · STEP 1 OF 9
Design a new type called SensorData — the blank card.
THE CARD D
Not made yet.
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Step 1 of 9. A struct design is like printing the blank card template.

## Slide 7: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 2 · STEP 2 OF 9
It has three members. Each is a float, with a comment saying its unit.
THE CARD D
Not made yet.
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: Step 2. The members are the boxes printed on the card.

## Slide 8: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 5 · STEP 3 OF 9
The ; after } ends the design. Nothing is stored yet.
THE CARD D
Not made yet.
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: Step 3. Forgetting this semicolon is a common Verify error.

## Slide 9: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 7 · STEP 4 OF 9
A function that hands back a whole SensorData.
THE CARD D
Not made yet.
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Step 4. A struct type can be a function's return type: three values from one call.

## Slide 10: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 8 · STEP 5 OF 9
Make one empty card, d.
THE CARD D
d.temperature = ?
d.humidity = ?
d.light = ?
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: Step 5. The card exists, but its boxes are not filled in yet.

## Slide 11: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 9 · STEP 6 OF 9
The dot reaches inside: fill in the temperature. Say it is 23.4.
THE CARD D
d.temperature = 23.4
d.humidity = ?
d.light = ?
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: Step 6. card dot member, like writing in one box on the card.

## Slide 12: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 10 · STEP 7 OF 9
Fill in the humidity: 51.
THE CARD D
d.temperature = 23.4
d.humidity = 51.0
d.light = ?
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: Step 7.

## Slide 13: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 11 · STEP 8 OF 9
Fill in the light: 700.
THE CARD D
d.temperature = 23.4
d.humidity = 51.0
d.light = 700.0
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: Step 8. Any of these could still be -1 if that sensor is not detected.

## Slide 14: Design the card, then fill it in.
Line by Line
1 struct SensorData {
2 float temperature; // °C
3 float humidity; // %
4 float light; // 0–1023
5 };
6
7 SensorData readAll() {
8 SensorData d;
9 d.temperature = incipe.getTemperature();
10 d.humidity = incipe.getHumidity();
11 d.light = incipe.getLightIntensity();
12 return d;
13 }
LINE 12 · STEP 9 OF 9
Hand back the whole card in one go.
THE CARD D
d.temperature = 23.4
d.humidity = 51.0
d.light = 700.0
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Step 9. One return, three values.

## Slide 15: One call, one card, every value.
Using It
1 SensorData now = readAll();
2 Serial.print(now.temperature);
3 Serial.print(" ");
4 Serial.println(now.light);
SERIAL MONITOR
23.40 700.00
With the values from the walkthrough.
STILL CHECK FOR −1
Each member can be −1 if its sensor is not detected. Check now.temperature >= 0 before you use it.
WHY BOTHER?
One function returns all three values. An array of SensorData keeps a whole log in order.
SIZE
12 bytes on the INCIPE Board: three floats of 4 bytes each.
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: M3 Session 1 builds its sensor dashboard on this idea.

## Slide 16: A state machine is a traffic light.
State Machines
At any moment it shows exactly one colour — never two, never none. After a set time it moves to the next colour, always in the same order.
A fixed list of states, and clear rules for each transition. FSM = finite state machine.
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: State: what the program is doing right now. Transition: moving from one state to the next.

## Slide 17: Give each state a name.
enum
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
Line | What it does
1 | A new type Light that can only be RED, YELLOW or GREEN.
2 | The light starts in the RED state.
The code now reads RED instead of a mystery number.
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: An enum is a list of named values.

## Slide 18: Write the machine as a table before you code it.
Plan First
State | Shows | Lasts | Next state
RED | Red | 3000 ms | YELLOW
YELLOW | Yellow | 1000 ms | GREEN
GREEN | Green | 3000 ms | RED
The curriculum order: Red → Yellow → Green → Red. Each row of the table becomes one case.
Real traffic lights differ from country to country. Change the table, and the code follows.
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: The table is the plan. Every later change starts here.

## Slide 19: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 1 · STEP 1 OF 8
Three named states.
VARIABLES
state = ?
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Step 1. RED, YELLOW and GREEN are the only values a Light can hold.

## Slide 20: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 2 · STEP 2 OF 8
Start in RED.
VARIABLES
state = RED
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: Step 2. Where the machine starts.

## Slide 21: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 5 · STEP 3 OF 8
First pass of loop(): which state are we in? RED.
VARIABLES
state = RED
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: Step 3. Every pass of loop() asks one question: which state am I in?

## Slide 22: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 6 · STEP 4 OF 8
Show red, wait 3 s, then move to YELLOW. break leaves the switch.
VARIABLES
state = YELLOW
SERIAL MONITOR
RED
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: Step 4. Show, wait, choose the next state — one row of the table.

## Slide 23: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 5 · STEP 5 OF 8
Next pass: state is YELLOW.
VARIABLES
state = YELLOW
SERIAL MONITOR
RED
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: Step 5. loop() runs again from the top.

## Slide 24: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 7 · STEP 6 OF 8
Show yellow for 1 s, then move to GREEN.
VARIABLES
state = GREEN
SERIAL MONITOR
RED
YELLOW
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: Step 6. The YELLOW row: 1000 ms, next GREEN.

## Slide 25: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 5 · STEP 7 OF 8
Next pass: GREEN.
VARIABLES
state = GREEN
SERIAL MONITOR
RED
YELLOW
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: Step 7. Third pass.

## Slide 26: The traffic light, one pass at a time.
Line by Line
1 enum Light { RED, YELLOW, GREEN };
2 Light state = RED;
3
4 void loop() {
5 switch (state) {
6 case RED: Serial.println("RED"); delay(3000); state = YELLOW; break;
7 case YELLOW: Serial.println("YELLOW"); delay(1000); state = GREEN; break;
8 case GREEN: Serial.println("GREEN"); delay(3000); state = RED; break;
9 }
10 }
LINE 8 · STEP 8 OF 8
Show green for 3 s, then back to RED — the cycle repeats.
VARIABLES
state = RED
SERIAL MONITOR
RED
YELLOW
GREEN
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Step 8. Back to RED. One full cycle: 3 + 1 + 3 = 7 seconds.

## Slide 27: Run it, extend it, count it.
Your Task
Step | Do this
1 | Add setup() with Serial.begin(9600);, Upload, and time one full cycle.
2 | Add a fourth state, RED_YELLOW, between RED and GREEN (shown as "RED + YELLOW" for 1 s), as many countries use. Update the table first, then the code.
3 | Keep a count of how many full cycles have run, and print it every time the light turns red.
On the LED strip: that version will be added once the Wiki page lists what incipe.setLEDcolour(...) and incipe.showLED() take. Each Serial.println is where the LED call will go.
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: Step 2 practises the rule: change the table first, then the code.

## Slide 28: Ask the AI to review your state machine.
AI Integration
PASTE YOUR CODE INTO THE WORKSPACE AI CHAT WITH
Review this traffic-light state machine. Check that every state has exactly one next state and that no state can be skipped or reached by mistake. Suggest up to three improvements and explain each in one sentence for a beginner. Do not rewrite the whole program.
The curriculum task: have AI review your FSM logic and suggest improvements.
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: The last sentence keeps the answer short enough to check.

## Slide 29: Check what comes back like a reviewer.
AI Integration
Ask yourself | Why
Does every suggested change still match my state table? | The table is the plan. Change the table first, then the code.
Did it add a default: case? | A good idea: if state ever holds something unexpected, go back to a safe state like RED.
Did it suggest millis() instead of delay()? | Useful later: with delay() the board cannot read a button during a light. M3 Session 4 covers it.
Did it rename my incipe.* calls or invent new ones? | Never accept that — compare with the Wiki.
© 2026 Incipe Academy Limited. All rights reserved.
29
Notes: Treat the AI as a reviewer, not the author.

## Slide 30: How many bytes is one SensorData?
Checkpoint 1
READ THE CODE
struct SensorData {
float temperature;
float humidity;
float light;
};
ANSWER
12
WHY
Three floats of 4 bytes each on the INCIPE Board.
© 2026 Incipe Academy Limited. All rights reserved.
30
Notes: Answer: 12.

## Slide 31: What prints?
Checkpoint 2
READ THE CODE
SensorData x;
x.temperature = 21.5;
Serial.println(x.temperature);
ANSWER
21.50
WHY
The dot reaches the temperature member; Arduino prints a float with two decimal places.
© 2026 Incipe Academy Limited. All rights reserved.
31
Notes: Answer: 21.50.

## Slide 32: The light starts in RED. What are the first four lines?
Checkpoint 3
READ THE CODE
case RED: ... state = YELLOW;
case YELLOW: ... state = GREEN;
case GREEN: ... state = RED;
ANSWER
RED
YELLOW
GREEN
RED
WHY
Each pass shows the current state, then moves on; after GREEN it goes back to RED.
© 2026 Incipe Academy Limited. All rights reserved.
32
Notes: Answer: RED, YELLOW, GREEN, RED.

## Slide 33: Which state comes straight after YELLOW?
Checkpoint 4
READ THE CODE
case YELLOW:
Serial.println("YELLOW");
delay(1000);
state = GREEN;
break;
ANSWER
GREEN
WHY
The YELLOW case sets state = GREEN.
© 2026 Incipe Academy Limited. All rights reserved.
33
Notes: Answer: GREEN.

## Slide 34: How long is one full Red → Yellow → Green cycle?
Checkpoint 5
READ THE CODE
case RED: ... delay(3000); ...
case YELLOW: ... delay(1000); ...
case GREEN: ... delay(3000); ...
ANSWER
7 s
WHY
3000 + 1000 + 3000 = 7000 ms.
© 2026 Incipe Academy Limited. All rights reserved.
34
Notes: Answer: 7 seconds.

## Slide 35: Three things to take away.
Recap
1
A struct groups related values under one name; reach each member with a dot, and return the whole card from a function.
2
A state machine is always in exactly one state; plan the states and transitions as a table, then write one case per row.
3
An enum gives states readable names — and the AI’s review should improve your table, not replace it.
Next — M3 Session 1: Analog sensors & ADC. How the board turns a voltage into a number, and a live Serial Monitor dashboard.
© 2026 Incipe Academy Limited. All rights reserved.
35
Notes: Homework: finish the traffic-light task, including the cycle count.