## Slide 1: Session 5 Input Devices: Joystick, IR & Buttons
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M3: Sensors & Modules
Notes: Session 5: read the joystick, find your own limits, act on the edge, and build the curriculum's joystick menu on the Serial Monitor.

## Slide 2: Turn a stick and a button into a menu you can steer.
Lesson Overview
Part | Topic | Time
01 | The joystick: read it, then find your limits | 8 min
02 | Zones and edges: one push, one move | 7 min
03 | Practice: a joystick menu on the Serial Monitor | 12 min
04 | The IR receiver: what is coming | 3 min
Builds on plotting the joystick in Session 2, arrays from Lesson 4, and switch and counting on release from M2 Session 2.
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Students need the board, the joystick, the push button, the temperature and humidity sensor and the light sensor.

## Slide 3: Five words you will hear today.
Key Words
Word | Plain meaning
Raw value | The number exactly as the module gives it, before you decide what it means.
Limit | A number you pick: past it, the stick counts as pushed.
Zone | Which part of its travel the stick is in: pushed one way, resting, or pushed the other way.
Edge | The moment something changes — the stick just got pushed, the button just got let go.
Wrap around | Going past the last menu item brings you back to the first, like the hands of a clock.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: Edge is the big idea of the session.

## Slide 4: A joystick is a game controller’s thumbstick.
The Joystick
Push it and the game moves; let go and it springs back to the middle.
The board can’t see “left” or “right” — it gets a number for how far the stick is pushed, and you decide what each number means.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: The meaning of the numbers is the student's job today.

## Slide 5: Three readings, one call each.
Meet the Joystick
ONE LINE OF CODE
float x = incipe.getJoystickXMovement();
float y = incipe.getJoystickYMovement();
float button = incipe.getJoystickButtonResponse();
Call | Value | Not detected
incipe.getJoystickXMovement() | A float, raw left–right position | -1
incipe.getJoystickYMovement() | A float, raw up–down position | -1
incipe.getJoystickButtonResponse() | A float, raw stick-button reading | -1
The range, the centre and which button value means “pressed” are not fixed — find them in the Serial Plotter. Leave the next connection free: the joystick uses it for Y and the button. Wiki › Joystick.
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: These facts are copied from the Wiki page and nothing more.

## Slide 6: Find your limits.
Try It
Step | Do this
1 | Plot X in the Serial Plotter, as in Session 2.
2 | Write down three numbers: X at rest, X pushed fully one way, X pushed fully the other way.
3 | Lower limit: halfway between rest and the smaller end. Upper limit: halfway between rest and the bigger end.
Today’s code uses 25 and 75 as stand-in limits so the examples are easy to follow. They are not your joystick’s numbers — replace them with yours.
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Halfway gives room for a wobbly hand: a small nudge stays resting, a real push counts.

## Slide 7: One push, one move — like a doorbell.
Zones and Edges
Holding a doorbell down rings it once, not a hundred times.
A menu should work the same way: one push of the stick moves one item, however long you hold it.
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: First we sort each reading into a zone, then we act only on the edge.

## Slide 8: Sort a reading into a zone.
Line by Line
1 const float LOW_LIMIT = 25; // change to your number
2 const float HIGH_LIMIT = 75; // change to your number
3
4 int zone(float x) {
5 if (x == -1) return 0; // not detected: treat as resting
6 if (x < LOW_LIMIT) return -1; // pushed one way
7 if (x > HIGH_LIMIT) return 1; // pushed the other way
8 return 0; // resting in the middle
9 }
LINE 1 · STEP 1 OF 6
Your lower limit. Below it, the stick is pushed one way.
VARIABLES
LOW_LIMIT = 25
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: const makes a value that never changes.

## Slide 9: Sort a reading into a zone.
Line by Line
1 const float LOW_LIMIT = 25; // change to your number
2 const float HIGH_LIMIT = 75; // change to your number
3
4 int zone(float x) {
5 if (x == -1) return 0; // not detected: treat as resting
6 if (x < LOW_LIMIT) return -1; // pushed one way
7 if (x > HIGH_LIMIT) return 1; // pushed the other way
8 return 0; // resting in the middle
9 }
LINE 2 · STEP 2 OF 6
Your upper limit. Above it, pushed the other way.
VARIABLES
LOW_LIMIT = 25
HIGH_LIMIT = 75
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Step 2.

## Slide 10: Sort a reading into a zone.
Line by Line
1 const float LOW_LIMIT = 25; // change to your number
2 const float HIGH_LIMIT = 75; // change to your number
3
4 int zone(float x) {
5 if (x == -1) return 0; // not detected: treat as resting
6 if (x < LOW_LIMIT) return -1; // pushed one way
7 if (x > HIGH_LIMIT) return 1; // pushed the other way
8 return 0; // resting in the middle
9 }
LINE 4 · STEP 3 OF 6
Call zone(90): x starts as 90.
VARIABLES
LOW_LIMIT = 25
HIGH_LIMIT = 75
x = 90
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: zone returns a whole number: -1, 0 or 1.

## Slide 11: Sort a reading into a zone.
Line by Line
1 const float LOW_LIMIT = 25; // change to your number
2 const float HIGH_LIMIT = 75; // change to your number
3
4 int zone(float x) {
5 if (x == -1) return 0; // not detected: treat as resting
6 if (x < LOW_LIMIT) return -1; // pushed one way
7 if (x > HIGH_LIMIT) return 1; // pushed the other way
8 return 0; // resting in the middle
9 }
LINE 5 · STEP 4 OF 6
Is x −1, “not detected”? No.
VARIABLES
LOW_LIMIT = 25
HIGH_LIMIT = 75
x = 90
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: The -1 rule: a missing joystick must never look like a push.

## Slide 12: Sort a reading into a zone.
Line by Line
1 const float LOW_LIMIT = 25; // change to your number
2 const float HIGH_LIMIT = 75; // change to your number
3
4 int zone(float x) {
5 if (x == -1) return 0; // not detected: treat as resting
6 if (x < LOW_LIMIT) return -1; // pushed one way
7 if (x > HIGH_LIMIT) return 1; // pushed the other way
8 return 0; // resting in the middle
9 }
LINE 6 · STEP 5 OF 6
Is 90 below 25? No.
VARIABLES
LOW_LIMIT = 25
HIGH_LIMIT = 75
x = 90
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: Step 5.

## Slide 13: Sort a reading into a zone.
Line by Line
1 const float LOW_LIMIT = 25; // change to your number
2 const float HIGH_LIMIT = 75; // change to your number
3
4 int zone(float x) {
5 if (x == -1) return 0; // not detected: treat as resting
6 if (x < LOW_LIMIT) return -1; // pushed one way
7 if (x > HIGH_LIMIT) return 1; // pushed the other way
8 return 0; // resting in the middle
9 }
LINE 7 · STEP 6 OF 6
Is 90 above 75? Yes — hand back 1: pushed.
VARIABLES
LOW_LIMIT = 25
HIGH_LIMIT = 75
x = 90
result = 1
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: return hands back the answer and leaves the function straight away.

## Slide 14: Act when the zone changes, not while it stays.
The Edge
THE PROBLEM
While you hold the stick, every pass of loop() sees zone 1 again — the menu would race through every item.
THE EDGE
Act only when the zone is not 0 now, but was 0 last pass: the stick was just pushed.
THE TRICK
Keep last pass’s zone in a variable, lastZone, and update it at the end of every pass.
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Same idea as counting a button on release in M2 Session 2.

## Slide 15: Build a joystick menu on the Serial Monitor.
Practice
The curriculum task: a simple menu system controlled by the Joystick and displayed on the Serial Monitor.
The menu is an array of three words; choice is the box you are on.
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: Arrays come from Lesson 4.

## Slide 16: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 1 · STEP 1 OF 19
A list of three menu items. Box 0 holds “Temperature”.
VARIABLES
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: const char* items[] is an array of pieces of text.

## Slide 17: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 2 · STEP 2 OF 19
Start on item 0.
VARIABLES
choice = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: Step 2.

## Slide 18: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 3 · STEP 3 OF 19
Last pass’s zone: resting.
VARIABLES
choice = 0
lastZone = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: Step 3.

## Slide 19: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 4 OF 19
Pass 1: the stick rests, the reading is 50, so the zone is 0.
VARIABLES
choice = 0
lastZone = 0
z = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Step 4.

## Slide 20: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 7 · STEP 5 OF 19
Is z not 0? No — skip the block. Line 13 keeps lastZone at 0.
VARIABLES
choice = 0
lastZone = 0
z = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: Step 5.

## Slide 21: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 6 OF 19
Pass 2: you push. The reading is 90, so the zone is 1.
VARIABLES
choice = 0
lastZone = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: Step 6.

## Slide 22: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 7 · STEP 7 OF 19
z is not 0 and lastZone is 0: it was just pushed. Go in.
VARIABLES
choice = 0
lastZone = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: && means and: both must be true.

## Slide 23: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 8 · STEP 8 OF 19
Move one item: 0 + 1.
VARIABLES
choice = 1
lastZone = 0
z = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: Step 8.

## Slide 24: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 11 · STEP 9 OF 19
Show the new item.
VARIABLES
choice = 1
lastZone = 0
z = 1
SERIAL MONITOR
Humidity
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: items[choice] is the text in that box.

## Slide 25: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 13 · STEP 10 OF 19
Remember this pass: pushed.
VARIABLES
choice = 1
lastZone = 1
z = 1
SERIAL MONITOR
Humidity
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: Step 10.

## Slide 26: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 11 OF 19
Pass 3: you are still holding. Zone 1 again.
VARIABLES
choice = 1
lastZone = 1
z = 1
SERIAL MONITOR
Humidity
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Step 11.

## Slide 27: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 7 · STEP 12 OF 19
lastZone is 1 — this push was already counted. Skip: one push, one move.
VARIABLES
choice = 1
lastZone = 1
z = 1
SERIAL MONITOR
Humidity
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: This is the edge at work.

## Slide 28: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 13 OF 19
Later: you let go (lastZone becomes 0), then push the other way. Reading 10: zone −1.
VARIABLES
choice = 1
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: Step 13.

## Slide 29: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 8 · STEP 14 OF 19
Move back: 1 + (−1).
VARIABLES
choice = 0
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
© 2026 Incipe Academy Limited. All rights reserved.
29
Notes: Step 14.

## Slide 30: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 11 · STEP 15 OF 19
Show it.
VARIABLES
choice = 0
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
Temperature
© 2026 Incipe Academy Limited. All rights reserved.
30
Notes: Step 15.

## Slide 31: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 6 · STEP 16 OF 19
Let go, then push that way again: zone −1.
VARIABLES
choice = 0
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
Temperature
© 2026 Incipe Academy Limited. All rights reserved.
31
Notes: Step 16.

## Slide 32: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 8 · STEP 17 OF 19
0 + (−1) is −1 — there is no box −1.
VARIABLES
choice = -1
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
Temperature
© 2026 Incipe Academy Limited. All rights reserved.
32
Notes: Step 17.

## Slide 33: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 10 · STEP 18 OF 19
Before the start: wrap to the end.
VARIABLES
choice = 2
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
Temperature
© 2026 Incipe Academy Limited. All rights reserved.
33
Notes: Wrap around at both ends so choice stays 0, 1 or 2.

## Slide 34: The menu, one pass at a time.
Line by Line
1 const char* items[] = {"Temperature", "Humidity", "Light"};
2 int choice = 0;
3 int lastZone = 0;
4
5 void loop() {
6 int z = zone(incipe.getJoystickXMovement());
7 if (z != 0 && lastZone == 0) { // just pushed
8 choice = choice + z;
9 if (choice > 2) choice = 0; // past the end: back to the start
10 if (choice < 0) choice = 2; // before the start: to the end
11 Serial.println(items[choice]);
12 }
13 lastZone = z;
14 delay(50);
15 }
LINE 11 · STEP 19 OF 19
Show it.
VARIABLES
choice = 2
lastZone = 0
z = -1
SERIAL MONITOR
Humidity
Temperature
Light
© 2026 Incipe Academy Limited. All rights reserved.
34
Notes: Put zone() above loop(), add setup() with Serial.begin(9600), and Upload.

## Slide 35: The push button answers yes or no.
Select with the Button
ONE LINE OF CODE
float pressed = incipe.getButtonResponse();
Button | You get
Pressed | 1
Not pressed | 0
Not detected | -1
Act when the button is released — the same edge idea as the stick. Wiki › Button.
© 2026 Incipe Academy Limited. All rights reserved.
35
Notes: Copied from the Button page of the Wiki.

## Slide 36: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 1 · STEP 1 OF 9
Last pass’s button reading: not pressed. The menu is on item 2, “Light”.
VARIABLES
lastButton = 0
choice = 2
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
36
Notes: Step 1.

## Slide 37: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 12 · STEP 2 OF 9
You press: b is 1.
VARIABLES
lastButton = 0
choice = 2
b = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
37
Notes: Step 2.

## Slide 38: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 13 · STEP 3 OF 9
Pressed last pass and released now? lastButton is 0 — no.
VARIABLES
lastButton = 0
choice = 2
b = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
38
Notes: Step 3.

## Slide 39: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 14 · STEP 4 OF 9
Remember: pressed.
VARIABLES
lastButton = 1
choice = 2
b = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
39
Notes: Step 4.

## Slide 40: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 12 · STEP 5 OF 9
You let go: b is 0.
VARIABLES
lastButton = 1
choice = 2
b = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
40
Notes: Step 5.

## Slide 41: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 13 · STEP 6 OF 9
Pressed last pass, released now — call showChoice().
VARIABLES
lastButton = 1
choice = 2
b = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
41
Notes: The release edge: 1 last pass, 0 now.

## Slide 42: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 4 · STEP 7 OF 9
Which item? choice is 2.
VARIABLES
lastButton = 1
choice = 2
b = 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
42
Notes: Step 7.

## Slide 43: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 7 · STEP 8 OF 9
case 2: print the light reading. Say it is 700.
VARIABLES
lastButton = 1
choice = 2
b = 0
SERIAL MONITOR
700.00
© 2026 Incipe Academy Limited. All rights reserved.
43
Notes: Each reading can still be -1 if its sensor is not detected.

## Slide 44: Show the chosen reading on release.
Line by Line
1 float lastButton = 0;
2
3 void showChoice() {
4 switch (choice) {
5 case 0: Serial.println(incipe.getTemperature()); break;
6 case 1: Serial.println(incipe.getHumidity()); break;
7 case 2: Serial.println(incipe.getLightIntensity()); break;
8 }
9 }
10
11 // inside loop(), after lastZone = z;
12 float b = incipe.getButtonResponse();
13 if (lastButton == 1 && b == 0) showChoice(); // on release
14 lastButton = b;
LINE 14 · STEP 9 OF 9
Back in loop(): remember, released.
VARIABLES
lastButton = 0
choice = 2
b = 0
SERIAL MONITOR
700.00
© 2026 Incipe Academy Limited. All rights reserved.
44
Notes: Step 9.

## Slide 45: Make the menu yours.
Your Task
Step | Do this
1 | Put your own limits into LOW_LIMIT and HIGH_LIMIT. If the menu moves the “wrong” way, swap what +1 and −1 do.
2 | Add a fourth item, “Distance”, that prints incipe.getDistance() from the ultrasonic sensor (in cm). Find every line that has to change — there are four places.
3 | Use the joystick’s own button instead of the push button. Plot incipe.getJoystickButtonResponse() first to find which value means “pressed”.
© 2026 Incipe Academy Limited. All rights reserved.
45
Notes: The four places in step 2: the items array, the two wrap-around lines, and a new case in showChoice().

## Slide 46: Decoding a TV remote is coming.
The IR Receiver
The IR receiver page on the Wiki says what the module does, but its incipe.* functions are not published yet.
This part will be added once they are — Session 7 builds on it.
© 2026 Incipe Academy Limited. All rights reserved.
46
Notes: Do not guess function names: wait for the Wiki page.

## Slide 47: With LOW_LIMIT 25 and HIGH_LIMIT 75, what does zone(90) return?
Checkpoint 1
READ THE CODE
zone(90);
ANSWER
1
WHY
90 is not −1 and not below 25, but it is above 75.
© 2026 Incipe Academy Limited. All rights reserved.
47
Notes: Answer: 1.

## Slide 48: The joystick is unplugged. What does zone(-1) return?
Checkpoint 2
READ THE CODE
zone(-1);
ANSWER
0
WHY
The first if catches −1 before it can count as “below 25”, so a missing joystick never moves the menu.
© 2026 Incipe Academy Limited. All rights reserved.
48
Notes: Answer: 0, resting.

## Slide 49: choice is 2 (“Light”). You push; the zone is 1. What prints?
Checkpoint 3
READ THE CODE
choice = choice + z;
if (choice > 2) choice = 0;
if (choice < 0) choice = 2;
Serial.println(items[choice]);
ANSWER
Temperature
WHY
2 + 1 is 3, past the end, so line 2 wraps choice to 0.
© 2026 Incipe Academy Limited. All rights reserved.
49
Notes: Answer: Temperature.

## Slide 50: You push and hold the stick for 10 passes. How many lines print?
Checkpoint 4
READ THE CODE
if (z != 0 && lastZone == 0) {
...
}
lastZone = z;
ANSWER
1
WHY
Only the first pass is an edge; on the other 9, lastZone is already 1.
© 2026 Incipe Academy Limited. All rights reserved.
50
Notes: Answer: 1.

## Slide 51: You hold the button for 3 passes, then let go. How many times does showChoice() run?
Checkpoint 5
READ THE CODE
if (lastButton == 1 && b == 0)
showChoice();
lastButton = b;
ANSWER
Once
WHY
Only on the pass where lastButton is 1 and b is 0.
© 2026 Incipe Academy Limited. All rights reserved.
51
Notes: Answer: once.

## Slide 52: Three things to take away.
Recap
1
The joystick gives raw numbers. Plot them, pick two limits, and sort every reading into a zone — with −1 counting as resting.
2
Act on the edge — just pushed, just released — so one push moves one item, however long you hold.
3
A menu is an array plus a choice number that wraps around at both ends; the button’s release edge selects.
Next — Session 6: Data logging with SD card. Saving readings to a file instead of only printing them.
© 2026 Incipe Academy Limited. All rights reserved.
52
Notes: Homework: finish the menu task, including the fourth item.