## Slide 1: Session 2 Control Structures & Functions
© 2026 Incipe Academy Limited.
All rights reserved.
Incipe 101
M2: Programming with C++
Notes: Session 2 picks up what Lessons 2 to 4 left out: switch, while and do-while, and writing your own functions. They come together in a Digital Dice that rolls when the button is pressed, and an AI-suggested debounce.

## Slide 2: Choose one of many, repeat until done, and give your code names.
Lesson Overview
Part | Topic | Time
01 | switch: one choice out of many | 6 min
02 | while and do-while: repeat until done | 6 min
03 | Writing your own functions | 7 min
04 | Practice: Digital Dice | 7 min
05 | AI integration: debouncing the button | 4 min
© 2026 Incipe Academy Limited. All rights reserved.
2
Notes: Five parts in thirty minutes. Students need the board and the button module.

## Slide 3: You know these from Lessons 2 to 4.
Already Covered
Idea | Where
if, else if, else, &&, ¦¦, ! | Lesson 2 · More about programming
Reading the button and counting a press on release | Lesson 3 · Programming sensors
for loops | Lesson 4 · Array & for loop
Today adds three new tools — switch, while / do-while and your own functions — and puts them to work in a Digital Dice.
© 2026 Incipe Academy Limited. All rights reserved.
3
Notes: Point students back to the M2 lessons for anything here they have forgotten. This session does not repeat them.

## Slide 4: Ten words you will hear today.
Key Words
Word | Plain meaning
switch | Picks one block of code to run, by matching a value exactly.
case | One possible value inside a switch.
break | "Stop here and leave the switch."
default | What runs when no case matches.
while | Repeats while a condition is true — checks first.
do-while | Runs once, then repeats while a condition is true — checks after.
Function | A named block of code you can run from anywhere by calling its name.
Parameter | A value you hand to a function when you call it.
Return value | The answer a function hands back.
Debounce | Ignoring the tiny flickers a button makes as it is pressed.
© 2026 Incipe Academy Limited. All rights reserved.
4
Notes: Read these aloud once; each one is explained again when it comes up.

## Slide 5: Like a vending machine: press 4, get slot 4.
switch
Not "bigger than 3", not "between 2 and 5" — exactly 4. A switch jumps straight to the case that equals the value.
Use switch when… | Use if / else if when…
You match exact values: 1, 2, 3… | You compare ranges: score >= 85
There are many choices of one variable | The conditions mix different variables
© 2026 Incipe Academy Limited. All rights reserved.
5
Notes: The grade example from Lesson 3 needs ranges, so it stays an if / else if. A dice face is an exact value, so it suits a switch.

## Slide 6: showDice() with a switch.
Line by Line
1 void showDice(int value) {
2 switch (value) {
3 case 1: Serial.println("one"); break;
4 case 2: Serial.println("two"); break;
5 case 3: Serial.println("three"); break;
6 case 4: Serial.println("four"); break;
7 case 5: Serial.println("five"); break;
8 case 6: Serial.println("six"); break;
9 default: Serial.println("not a dice number");
10 }
11 }
LINE 1 · STEP 1 OF 6
showDice takes one number. Say we call showDice(4).
VARIABLES
value = 4
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
6
Notes: Step 1 of 6. A function with one int parameter, value. We follow the call showDice(4).

## Slide 7: showDice() with a switch.
Line by Line
1 void showDice(int value) {
2 switch (value) {
3 case 1: Serial.println("one"); break;
4 case 2: Serial.println("two"); break;
5 case 3: Serial.println("three"); break;
6 case 4: Serial.println("four"); break;
7 case 5: Serial.println("five"); break;
8 case 6: Serial.println("six"); break;
9 default: Serial.println("not a dice number");
10 }
11 }
LINE 2 · STEP 2 OF 6
switch (value) — find the case that equals 4.
VARIABLES
value = 4
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
7
Notes: Step 2. The switch looks at value and jumps to the matching case. It does not test the cases one by one like an if chain.

## Slide 8: showDice() with a switch.
Line by Line
1 void showDice(int value) {
2 switch (value) {
3 case 1: Serial.println("one"); break;
4 case 2: Serial.println("two"); break;
5 case 3: Serial.println("three"); break;
6 case 4: Serial.println("four"); break;
7 case 5: Serial.println("five"); break;
8 case 6: Serial.println("six"); break;
9 default: Serial.println("not a dice number");
10 }
11 }
LINE 6 · STEP 3 OF 6
case 4 matches. Print "four"…
VARIABLES
value = 4
SERIAL MONITOR
four
© 2026 Incipe Academy Limited. All rights reserved.
8
Notes: Step 3. The switch jumped straight to case 4 and printed four.

## Slide 9: showDice() with a switch.
Line by Line
1 void showDice(int value) {
2 switch (value) {
3 case 1: Serial.println("one"); break;
4 case 2: Serial.println("two"); break;
5 case 3: Serial.println("three"); break;
6 case 4: Serial.println("four"); break;
7 case 5: Serial.println("five"); break;
8 case 6: Serial.println("six"); break;
9 default: Serial.println("not a dice number");
10 }
11 }
LINE 6 · STEP 4 OF 6
…then break jumps out of the switch. Cases 5, 6 and default are skipped.
VARIABLES
value = 4
SERIAL MONITOR
four
© 2026 Incipe Academy Limited. All rights reserved.
9
Notes: Step 4. break is what stops the code from running on into case 5. Without it, the next cases would run too.

## Slide 10: showDice() with a switch.
Line by Line
1 void showDice(int value) {
2 switch (value) {
3 case 1: Serial.println("one"); break;
4 case 2: Serial.println("two"); break;
5 case 3: Serial.println("three"); break;
6 case 4: Serial.println("four"); break;
7 case 5: Serial.println("five"); break;
8 case 6: Serial.println("six"); break;
9 default: Serial.println("not a dice number");
10 }
11 }
LINE 10 · STEP 5 OF 6
Leave the switch.
VARIABLES
value = 4
SERIAL MONITOR
four
© 2026 Incipe Academy Limited. All rights reserved.
10
Notes: Step 5. The closing brace of the switch.

## Slide 11: showDice() with a switch.
Line by Line
1 void showDice(int value) {
2 switch (value) {
3 case 1: Serial.println("one"); break;
4 case 2: Serial.println("two"); break;
5 case 3: Serial.println("three"); break;
6 case 4: Serial.println("four"); break;
7 case 5: Serial.println("five"); break;
8 case 6: Serial.println("six"); break;
9 default: Serial.println("not a dice number");
10 }
11 }
LINE 11 · STEP 6 OF 6
The function ends. A value like 7 or 0 would have matched no case and run default instead.
VARIABLES
value = 4
SERIAL MONITOR
four
© 2026 Incipe Academy Limited. All rights reserved.
11
Notes: Step 6. Always give a switch a default, so a value you did not expect still does something visible.

## Slide 12: Forget a break and the code falls through.
Be Careful
Without break, C++ keeps running into the next case until it meets one. That is almost always a bug — Checkpoint 2 shows what happens.
© 2026 Incipe Academy Limited. All rights reserved.
12
Notes: End every case with break. The Verify button does not warn you about a missing break; it is a logical error, not a syntax error.

## Slide 13: One cook checks first. The other tastes first.
while & do-while
"While the water isn't boiling, wait" checks before acting: that is while. "Taste the soup, then decide if it needs salt" acts first: that is do-while.
Loop | Checks | Runs at least once? | Best for
for | Before each pass | No | Counting a known number of times (Lesson 4)
while | Before each pass | No | "Keep going until something happens"
do-while | After each pass | Yes | "Do it once, then repeat if needed"
© 2026 Incipe Academy Limited. All rights reserved.
13
Notes: Lesson 2 used while (Serial.available() == 0) {} to wait for typing; that is a while loop with an empty body. Today we give it a body.

## Slide 14: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 1 · STEP 1 OF 12
Start the countdown at 3.
VARIABLES
count = 3
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
14
Notes: Step 1 of 12. A countdown before the dice roll: 3, 2, 1, Roll!

## Slide 15: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 2 · STEP 2 OF 12
Is 3 > 0? Yes — go in.
VARIABLES
count = 3
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
15
Notes: Step 2. A while loop checks its condition before every pass, including the first one.

## Slide 16: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 3 · STEP 3 OF 12
Print the count.
VARIABLES
count = 3
SERIAL MONITOR
3
© 2026 Incipe Academy Limited. All rights reserved.
16
Notes: Step 3. The first line of output: 3.

## Slide 17: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 4 · STEP 4 OF 12
Take 1 away — otherwise the loop would never end.
VARIABLES
count = 3 → 2
SERIAL MONITOR
3
© 2026 Incipe Academy Limited. All rights reserved.
17
Notes: Step 4. Forgetting this line is the classic infinite loop: count would stay 3 forever.

## Slide 18: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 2 · STEP 5 OF 12
Back to the check. Is 2 > 0? Yes.
VARIABLES
count = 3 → 2
SERIAL MONITOR
3
© 2026 Incipe Academy Limited. All rights reserved.
18
Notes: Step 5. The closing brace sends the program back up to the while check.

## Slide 19: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 3 · STEP 6 OF 12
Print it.
VARIABLES
count = 3 → 2
SERIAL MONITOR
3
2
© 2026 Incipe Academy Limited. All rights reserved.
19
Notes: Step 6. Second line of output: 2.

## Slide 20: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 4 · STEP 7 OF 12
Take 1 away.
VARIABLES
count = 3 → 2 → 1
SERIAL MONITOR
3
2
© 2026 Incipe Academy Limited. All rights reserved.
20
Notes: Step 7. count is now 1.

## Slide 21: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 2 · STEP 8 OF 12
Is 1 > 0? Yes.
VARIABLES
count = 3 → 2 → 1
SERIAL MONITOR
3
2
© 2026 Incipe Academy Limited. All rights reserved.
21
Notes: Step 8. One more pass.

## Slide 22: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 3 · STEP 9 OF 12
Print it.
VARIABLES
count = 3 → 2 → 1
SERIAL MONITOR
3
2
1
© 2026 Incipe Academy Limited. All rights reserved.
22
Notes: Step 9. Third line of output: 1.

## Slide 23: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 4 · STEP 10 OF 12
Take 1 away.
VARIABLES
count = 3 → 2 → 1 → 0
SERIAL MONITOR
3
2
1
© 2026 Incipe Academy Limited. All rights reserved.
23
Notes: Step 10. count reaches 0.

## Slide 24: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 2 · STEP 11 OF 12
Is 0 > 0? No — skip the loop.
VARIABLES
count = 3 → 2 → 1 → 0
SERIAL MONITOR
3
2
1
© 2026 Incipe Academy Limited. All rights reserved.
24
Notes: Step 11. 0 is not greater than 0, so the condition is false and the loop is over.

## Slide 25: A while-loop countdown.
Line by Line
1 int count = 3;
2 while (count > 0) {
3 Serial.println(count);
4 count = count - 1;
5 }
6 Serial.println("Roll!");
LINE 6 · STEP 12 OF 12
Carry on after the loop.
VARIABLES
count = 3 → 2 → 1 → 0
SERIAL MONITOR
3
2
1
Roll!
© 2026 Incipe Academy Limited. All rights reserved.
25
Notes: Step 12. The full output: 3, 2, 1, Roll!

## Slide 26: A do-while always runs at least once.
do-while
int n = 10;
do {
Serial.println(n);
n = n + 1;
} while (n < 5);
Line | What it does
1 | n starts at 10.
2–4 | The body runs first: prints 10, then n becomes 11.
5 | Now it checks n < 5. 11 is not less than 5, so it stops. It printed once.
The same loop written with while would print nothing: 10 < 5 is false before the first pass.
© 2026 Incipe Academy Limited. All rights reserved.
26
Notes: Taste first, then check. Use do-while when the body must happen at least once, for example asking a question before checking the answer.

## Slide 27: A function is a recipe card with a name.
Your Own Functions
It has a name ("Pancakes"), ingredients you bring (parameters) and a dish you get back (the return value). Once written, anyone can say "make pancakes".
Part | Meaning
int (the first word) | The type of the answer it hands back. void means "hands nothing back".
addDice | The function's name — say what it does.
(int a, int b) | Two parameters: the ingredients.
return a + b; | Hand back the answer, and leave the function.
addDice(3, 4) | The call: 3 goes into a, 4 into b.
© 2026 Incipe Academy Limited. All rights reserved.
27
Notes: Students have been calling functions all along: Serial.println, incipe.getButtonResponse. Now they write one. A function gives a few lines a name, so loop() reads like a sentence.

## Slide 28: Calling addDice().
Line by Line
1 int addDice(int a, int b) {
2 return a + b;
3 }
4
5 void setup() {
6 Serial.begin(9600);
7 int total = addDice(3, 4);
8 Serial.println(total);
9 }
LINE 6 · STEP 1 OF 5
The board starts in setup(). Start the Serial monitor.
VARIABLES
None yet.
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
28
Notes: Step 1 of 5. Writing addDice above setup does not run it. A function only runs when something calls it.

## Slide 29: Calling addDice().
Line by Line
1 int addDice(int a, int b) {
2 return a + b;
3 }
4
5 void setup() {
6 Serial.begin(9600);
7 int total = addDice(3, 4);
8 Serial.println(total);
9 }
LINE 7 · STEP 2 OF 5
Call addDice with 3 and 4. Jump up to the function.
VARIABLES
a = 3
b = 4
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
29
Notes: Step 2. The values in the call go into the parameters in order: 3 into a, 4 into b.

## Slide 30: Calling addDice().
Line by Line
1 int addDice(int a, int b) {
2 return a + b;
3 }
4
5 void setup() {
6 Serial.begin(9600);
7 int total = addDice(3, 4);
8 Serial.println(total);
9 }
LINE 2 · STEP 3 OF 5
Work out 3 + 4 and hand the answer back with return.
VARIABLES
a = 3
b = 4
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
30
Notes: Step 3. return hands back 7 and leaves the function straight away.

## Slide 31: Calling addDice().
Line by Line
1 int addDice(int a, int b) {
2 return a + b;
3 }
4
5 void setup() {
6 Serial.begin(9600);
7 int total = addDice(3, 4);
8 Serial.println(total);
9 }
LINE 7 · STEP 4 OF 5
Back in setup(): the answer goes into total.
VARIABLES
a = 3, b = 4
total = 7
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
31
Notes: Step 4. The call addDice(3, 4) is replaced by its answer, 7.

## Slide 32: Calling addDice().
Line by Line
1 int addDice(int a, int b) {
2 return a + b;
3 }
4
5 void setup() {
6 Serial.begin(9600);
7 int total = addDice(3, 4);
8 Serial.println(total);
9 }
LINE 8 · STEP 5 OF 5
Print it.
VARIABLES
a = 3, b = 4
total = 7
SERIAL MONITOR
7
© 2026 Incipe Academy Limited. All rights reserved.
32
Notes: Step 5. The Serial monitor shows 7. Fix a bug inside a function once, and every call is fixed.

## Slide 33: Press the button, roll a number from 1 to 6.
Practice: Digital Dice
ONE LINE OF CODE
float pressed = incipe.getButtonResponse();
Button | You get
Pressed | 1
Not pressed | 0
Not detected | -1
The button needs no data cleaning — it already answers yes or no. Full details: Wiki › Button.
© 2026 Incipe Academy Limited. All rights reserved.
33
Notes: The curriculum practice: press the button and display a random number. Three pieces: roll, show, and the button. These are the button facts from the Wiki, nothing more.

## Slide 34: random(1, 7) gives 1 up to, but not including, 7.
Piece 1 — Roll
int rollDice(int sides) {
return random(1, sides + 1);
}
Line | What it does
1 | Takes how many sides the dice has; returns a whole number.
2 | random(1, 7) picks 1 to 6. That is why it says sides + 1.
3 | End of the function.
Piece 2 — show: showDice(value) from the switch. Piece 3 — the button: count a roll on release, as in Lesson 3. On the LED strip: added once the Wiki lists what its functions take.
© 2026 Incipe Academy Limited. All rights reserved.
34
Notes: The curriculum shows the dice on the LED strip, one LED per pip. The Wiki does not yet list what incipe.setLEDcolour and incipe.showLED take, so today the Serial monitor is the display.

## Slide 35: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 1 · STEP 1 OF 9
Remember whether the button is being held. At the start it is not.
VARIABLES
pressed = false
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
35
Notes: Step 1 of 9. The same release logic as Lesson 3, now calling our two functions.

## Slide 36: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 4 · STEP 2 OF 9
Read the button. Say it is being pressed.
VARIABLES
pressed = false
button = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
36
Notes: Step 2. getButtonResponse gives 1 while the button is held.

## Slide 37: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 5 · STEP 3 OF 9
It is 1, so…
VARIABLES
pressed = false
button = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
37
Notes: Step 3. The if condition is true.

## Slide 38: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 6 · STEP 4 OF 9
…remember that it is held. Nothing is rolled yet.
VARIABLES
pressed = false → true
button = 1
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
38
Notes: Step 4. While the button is held, loop runs many times; each pass just keeps pressed true.

## Slide 39: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 4 · STEP 5 OF 9
loop() runs again. Now the button has been let go.
VARIABLES
pressed = false → true
button = 1 → 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
39
Notes: Step 5. The button now reads 0, but pressed still remembers the press.

## Slide 40: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 7 · STEP 6 OF 9
It is 0 and it was held — so this is a release.
VARIABLES
pressed = false → true
button = 1 → 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
40
Notes: Step 6. A minus one reading matches neither branch, so an unplugged button rolls nothing.

## Slide 41: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 8 · STEP 7 OF 9
Forget the press, so one press makes one roll.
VARIABLES
pressed = false → true → false
button = 1 → 0
SERIAL MONITOR
© 2026 Incipe Academy Limited. All rights reserved.
41
Notes: Step 7. Resetting pressed is what stops one press turning into many rolls.

## Slide 42: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 9 · STEP 8 OF 9
Roll a 6-sided dice and show it. Say it rolled 4.
VARIABLES
pressed = false → true → false
button = 1 → 0
SERIAL MONITOR
four
© 2026 Incipe Academy Limited. All rights reserved.
42
Notes: Step 8. rollDice(6) runs first and gives a number from 1 to 6; that number goes straight into showDice. The roll is random; 4 is just an example.

## Slide 43: Piece 3 — roll on release.
Line by Line
1 bool pressed = false;
2
3 void loop() {
4 float button = incipe.getButtonResponse();
5 if (button == 1) {
6 pressed = true;
7 } else if (button == 0 && pressed) {
8 pressed = false;
9 showDice(rollDice(6));
10 }
11 }
LINE 4 · STEP 9 OF 9
Next pass: still 0, but pressed is false, so nothing happens until the next press.
VARIABLES
pressed = false → true → false
button = 1 → 0
SERIAL MONITOR
four
© 2026 Incipe Academy Limited. All rights reserved.
43
Notes: Step 9. One press, one roll.

## Slide 44: Put the three pieces in one sketch.
Try It
Write rollDice(sides) and showDice(value) at the top.
Add setup() with Serial.begin(9600);
Add bool pressed = false; and the loop() from the walkthrough.
Verify, then Upload. Open the Serial monitor at 9600.
Press and release the button: one press, one roll. Unplug it: nothing rolls.
© 2026 Incipe Academy Limited. All rights reserved.
44
Notes: Functions must be written above the place they are first used, or declared there. Putting rollDice and showDice at the top keeps it simple.

## Slide 45: Ask the AI to debounce the button.
AI Integration
Real buttons flicker 1-0-1-0 for a few milliseconds before they settle. That is bounce, and it can turn one press into several rolls.
Prompt: My Digital Dice reads incipe.getButtonResponse() in loop() and rolls when the button is released. Suggest a way to debounce the button. Keep my release logic, explain each line for a beginner, and say what happens if the button returns -1.
© 2026 Incipe Academy Limited. All rights reserved.
45
Notes: The curriculum's AI task: use AI to suggest error handling for button debouncing. The prompt names the exact function, asks the AI to keep the student's logic, and asks about minus one.

## Slide 46: Trust a reading once it has been steady for 50 ms.
A Typical Answer
1 const unsigned long DEBOUNCE_MS = 50;
2 unsigned long changedAt = 0;
3 float lastReading = 0;
4
5 void loop() {
6 float reading = incipe.getButtonResponse();
7 if (reading != lastReading) {
8 changedAt = millis();
9 lastReading = reading;
10 }
11 if (millis() - changedAt > DEBOUNCE_MS) {
12 // steady for 50 ms: trust it here
13 }
14 }
Line | What it does
1 | A reading must stay the same for 50 ms.
2 | When it last changed. millis() counts ms since the board started; it needs an unsigned long.
7–10 | If it changed, note the time and the new reading.
11–13 | Only after 50 ms steady, act on it — put the release logic here.
© 2026 Incipe Academy Limited. All rights reserved.
46
Notes: Review it like M1 Session 2: is the incipe name exactly the Wiki's? What does minus one do here? It is just another value, so an unplugged button settles at minus one and still rolls nothing. Did the AI keep the release logic, or rewrite it?

## Slide 47: What do showDice(3) and showDice(7) print?
Checkpoint 1
READ THE CODE
switch (value) {
case 1: …
case 3: Serial.println("three"); break;
…
case 6: …
default: Serial.println("not a dice number");
}
ANSWER
three
not a dice number
WHY
3 matches case 3. 7 matches no case, so default runs.
© 2026 Incipe Academy Limited. All rights reserved.
47
Notes: Answer: three, then not a dice number.

## Slide 48: case 2 has no break. What does a value of 2 print?
Checkpoint 2
READ THE CODE
switch (value) {
case 1: Serial.println("one"); break;
case 2: Serial.println("two");
case 3: Serial.println("three"); break;
default: Serial.println("?");
}
ANSWER
two
three
WHY
Without a break, case 2 falls through into case 3 and stops at its break.
© 2026 Incipe Academy Limited. All rights reserved.
48
Notes: Answer: two, then three. This was run and checked; fall-through is real C++ behaviour.

## Slide 49: What does this while loop print?
Checkpoint 3
READ THE CODE
int count = 3;
while (count > 0) {
Serial.println(count);
count = count - 1;
}
ANSWER
3
2
1
WHY
When count reaches 0, 0 > 0 is false and the loop stops.
© 2026 Incipe Academy Limited. All rights reserved.
49
Notes: Answer: 3, 2, 1 on three lines.

## Slide 50: What does this do-while loop print?
Checkpoint 4
READ THE CODE
int n = 10;
do {
Serial.println(n);
n = n + 1;
} while (n < 5);
ANSWER
10
WHY
Printed once. A do-while runs its body before it checks; then 11 < 5 is false.
© 2026 Incipe Academy Limited. All rights reserved.
50
Notes: Answer: 10, once. A plain while loop would print nothing.

## Slide 51: Which numbers can rollDice(6) return?
Checkpoint 5
READ THE CODE
int rollDice(int sides) {
return random(1, sides + 1);
}
ANSWER
1, 2, 3, 4, 5 or 6
WHY
random(1, 7) includes 1 but stops before 7.
© 2026 Incipe Academy Limited. All rights reserved.
51
Notes: Answer: any whole number from 1 to 6. A common mistake is random(1, 6), which can never give a 6.

## Slide 52: Three things to take away.
Recap
1
switch jumps to the case that equals a value. End every case with break, and add a default.
2
while checks first; do-while runs once, then checks; for counts.
3
A function has a name, parameters in and a return value out — so loop() can read showDice(rollDice(6)).
Next — Session 3: Arrays, pointers & bitwise operations. Store ten light readings, find a moving average, and look inside a byte.
© 2026 Incipe Academy Limited. All rights reserved.
52
Notes: Three points to remember. Homework: finish the Digital Dice and add the AI's debounce, reviewed line by line.