## Slide 1: Lesson 5 Recap
© 2026 Incipe Academy Limited. All rights reserved.
Taster Workshop
Programming with C++
Notes: A recap of Lessons 1 to 4 with six checkpoints, then the minigame classwork.

## Slide 2: Everything from Lessons 1 to 4.
2
Lesson Overview
01
Data types & errors
02
Showing data on the INCIPE Board screen
03
Input, compare & decide
04
Sensors & data cleaning
05
Arrays & for loops
06
Classwork: make a minigame
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 3: Six data types.
3
Data Types
Type | Meaning | Example
Integer | Integer in Maths, can be positive, 0 or negative | 1, 102
Float | Numbers that can have up to 7 decimal places | 1.234, 2.345
Double | Numbers that can have up to 15 decimal places | 1.234567890123
Char | Single character | A
String | Multiple characters | ABC, Hello
Boolean | A data type whose value is either true or false | true, false
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Teacher note: on AVR boards such as the Arduino Mega, double is stored the same way as float.

## Slide 4: Syntax, run-time & logic errors.
4
Errors
Syntax error
Written mistakes, eg a missing “;” or bracket.
Run-time error
The computer could not perform what you tell it to do, eg 1/0.
Logic error
The code runs, but the outcome is not what you expected.
LOGIC ERROR EXAMPLE
if (sensorValue > threshold) {
Print("true"); }
else if (sensorValue < threshold) {
Print("false"); }
Nothing would be performed when sensorValue = threshold.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 5: Which is the correct format for creating a variable?
5
Checkpoint 1
READ THE CODE
type name = value;
int a = 10;
float t = 25.5;
String s = "Hi";
ANSWER
int a = 10;
WHY
Data type first, then the variable name, then = and a value, and end with “;”.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The original Slido options were not in the source deck; the answer gives the correct format.

## Slide 6: Getting input into the program.
8
Input · Process · Output
Input
Data that goes into the program
Process
What the program does with the data
Output
The result shown to the user
WITHOUT A LIBRARY
while (Serial.available() == 0) {}
int n = Serial.parseInt();
float f = Serial.parseFloat();
WITH THE INCIPE LIBRARY
incipe.getTemperature();
incipe.getLightIntensity();
incipe.getDistance();
© 2026 Incipe Academy Limited. All rights reserved.
Notes: while (Serial.available() == 0) {} waits until the user types something in the serial monitor.

## Slide 7: Three questions, three steps.
9
Mini Calculator
1
How to ask users to input two numbers? How to store them?
Serial.println("Please type your first number.");
while(Serial.available()==0){}
int a = Serial.parseInt();
2
How to add the two numbers? Store it to where?
int sum = a+b;
3
How to show the answer?
Serial.print("The answer is:");
Serial.println(sum);
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The second number is read the same way and stored in b.

## Slide 8: Compare, combine, decide.
10
Compare & Decide
COMPARE
Symbol | Meaning
== | Equals to
!= | Not equals to
<= | Smaller than or equal to
>= | Larger than or equal to
< | Smaller than
> | Larger than
Remember: = assigns a value; == compares two values.
COMBINE
&&
AND: both must be true
||
OR: any one is true
!
NOT
DECIDE
if (…) { } else if (…) { } else { }
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 9: What is the value of data?
11
Checkpoint 3
READ THE CODE
int data = 8;
if (data < 5) {
data = data + 5;
}
else if (data > 8) {
data = data - 3;
}
else {
data++;
}
ANSWER
9
WHY
8 < 5 is false and 8 > 8 is false, so the else runs: data++ makes 8 into 9.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The source code has no print line; the answer is the value of data after the if-else.

## Slide 10: Which values make this true?
12
Checkpoint 4
READ THE CODE
(x > y) && !(y >= z)
ANSWER
x=3, y=1, z=2
WHY
Both sides of && must be true: x > y, and !(y >= z) means y < z. Any x > y with y < z works.
© 2026 Incipe Academy Limited. All rights reserved.
Notes: The original Slido options were not in the source deck; one valid example is given.

## Slide 11: Sensor readings need cleaning.
13
Sensors
FUNCTIONS FOR SENSORS
incipe.getTemperature()
incipe.getHumidity()
incipe.getDistance()
incipe.getLightIntensity()
incipe.getPPM()
incipe.getCOPPM()
incipe.getAlcoholPPM()
incipe.getFlameIntensity()
DATA CLEANING
Fixing or removing incorrect or incomplete raw data. Here, we focus on interpreting the raw data to make it more useful.
if AQvalue < xxxx
print Good
else if AQvalue > xxxx and < xxxx
print Moderate
else
print Poor
© 2026 Incipe Academy Limited. All rights reserved.
Notes: Sensors are review examples. The button counter and sound sensor sketch are not repeated here.

## Slide 12: Create an array: type, name, size.
14
Array
int data[6];
int array with a size of 6, without existing data
int value[5] = {2, 4, -8, 3, 2};
int array with a size of 5, with existing data
float number[2] = {2.8943, 10.23189};
You can use other data types too: float, size of 2
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 13: Write, read & clear by index.
15
Array
Write
int data[6] = {1,2,3,4,5,6};
data[1] = 10;
→ {1,10,3,4,5,6}
data[1] is the second element. To change the first, use [0].
Read
int data[6] = {1,10,3,4,5,6};
x = data[4];
→ x = 5
x gets a copy of the fifth element. The array does not change.
Clear
int data[6] = {1,10,3,4,5,6};
data[5] = 0;
→ {1,10,3,4,5,0}
We assume 0 means nothing, so this removes the sixth element.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 14: What is in the array now?
16
Checkpoint 5
READ THE CODE
int array[5] = {1, 3, 5, 7, 9};
array[1] = array[2] + 3;
array[4] = array[3] - 2;
ANSWER
{1, 8, 5, 7, 5}
WHY
array[1] = 5 + 3 = 8 and array[4] = 7 - 2 = 5. Index starts at 0.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 15: Repeat a command with a fixed structure.
17
For Loop
A for loop repeats some command. It is mainly used to control arrays.
for (int i = 0; i <= 25; i++)
{
Serial.println(i);
}
int i = 0
Initial value of a variable to control the loop
i <= 25
Used to determine the end of the loop
i++
Change of the value after each loop (i++ adds 1)
© 2026 Incipe Academy Limited. All rights reserved.
Notes: This prints 0, 1, 2 … up to 25, each on a new line: 26 lines in total.

## Slide 16: Use i as the index.
18
For Loop + Array
int data[5] = {0,1,2,3,4};
void setup() {
Serial.begin(9600);
}
void loop() {
for (int i = 0; i < 5; i = i+1)
{
Serial.println(data[i]);
delay(1000);
}
}
i = 0
Initial value of i is 0, the first index
i < 5
Limit i to below 5, the size of the array
data[i]
Prints data[0] the 1st time, data[1] the 2nd time, and so on
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 17: What is the value of a?
19
Checkpoint 6
READ THE CODE
int a = 20;
int number[5] = {1, 3, 5, 2, 4};
for (int i = 0; i < 4; i++) {
a = a - number[i];
}
ANSWER
9
WHY
i runs 0 to 3, so a = 20 − 1 − 3 − 5 − 2 = 9. number[4] is never used.
© 2026 Incipe Academy Limited. All rights reserved.

## Slide 18: Lessons 1 to 4, done.
21
Recap
Today we reviewed data types, errors, onscreen, input, if-else and logic, sensors, arrays and for loops.
Thank you!
© 2026 Incipe Academy Limited. All rights reserved.